# 船舶轮机英语集成

第      1   页

船舶英语                                                                  27．压缩环  (气环)       Compression ring

目 录                                                                28．刮油环  (油环)       Oil scraper ring

一.职位及工种                                    一．职位及工种(Titles and type of work)          29．减磨令          Wear ring  (copper ring)

(Titles and type of work)      ····· 1     1．船长           Captain                    30．伸缩管(水拉管)  Telescopic pipe

二、柴油机类                                     2．大副           Chief officer              31．活塞冷却空间   Piston cooling space

(Words about diesel engine)    ····· 3     3．二副           Second officer             32．填料箱 (函)       Stuffing box

三、船舶机械类                                    4．三副           Third officer              33．填料箱密封环 Sealing ring for Stuffing

(Words about marine machinery)    ·· 11    5．四副           Fourth officer             box

四、阀门(Words about valve)         ···· 14    6．水手长          Boatswain                  34．填料箱压缩环 Pressure ring for Stuffing

五、泵类(Words about pump)  ·········· 16      7．水手           Sailor & Seaman            box

六、甲板机械类（Deck machinery） ······ 18          8．木匠           Carpenter                  35．填料箱刮油环 Scraper ring for Stuffing

七、工具类(Word about tools)  ········ 20       9．轮机长          Chief engineer             box

八、常用物料(Material in common use)       26    10．大管轮         Second engineer            36．扫气箱           Scavenging receiver

九、常用紧固件                                    11．二管轮         Third engineer             37．扫气口           Scavenging port

(Part of fixation in common use)  ··· 28   12．三管轮         Fourth engineer            38．排气口          Exhaust port

十、常用油类(Oil in common use)  ·····28         13．机匠长         Chief motorman             39．十字头          Cross head

十一、常用量词                                    15．机匠          Fitter                     40．十字头销         Crosshead pin

(Quantifier in common use)  ·········29    16．加油工         Oil man                    41．十字头轴承   Crosshead bearing

十二、国家名称(Name of  country)  。 30            17．大电          Chief electrician          42．十字头滑块   Crosshead slipper

十三、常用缩语                                    18．电工          Electrician                43．滑块           Guide shoe

(abbreviation in common use)   ·····31     19．车间主任        Workshop director          44．十字头导板  Crosshead guide plate

20．工长          Section chief              45．连杆           Connecting rod

十四、船用动态常用单词 (marine tends word)                                                                              4

32                                         21．班长          Fore man                   46．连杆大端轴承  Bid end bearing

十五、船舶机电设备操作词汇                              22．钳工          Fitter                     47．连杆小端轴承  Small end bearing

(manipulate of marine equipment)  ·33      23．主管工程师  Engineer in charge              48．曲柄轴承         Crank bearing

十六、故障常用单词                                  24 ．机 务 & 船东        Superintendent  &Super  49．曲柄销        Crank pin

(words about malfunction)    ····· 35      &Owner                                    50．曲轴           Crank shaft

十七、保养检修常用词汇                                25．助理工程师  Assistant engineer              51．曲轴颈          Crank journal

(Words about maintain and examination) 38  26．验船师 （机）Register                        52．曲柄臂          Crank web

十八、常用数字(Numeral in common use) 40          27．验船师 （船）Surveyor                        53．拐档差          Crank deflection

十九、时间、季节与方向                                28．油漆工         Painter                    54．主轴承          Main bearing

(Time、Season and Direction)  ·····42    29．焊工          Welder                     55．主轴颈          Main journal

二十常用词组 （Phrases in common use） ·45         30．大橱          Chief cook                 56．轴承瓦          Bearing bush

二十一、常用动词和例句                                31．物料员         Store keeper               57．上轴瓦          Upper bearing bush

(Verb in common use and example)  ····48   32．加油工         Oiler                      58．上轴瓦          Upper half

二十二、问候和常用表达语                               33．机工          Mechanic                   59．下轴瓦          Lower bearing bush

(Greeting and common expression)  ····67   34．甲板员         Deck man                   60．下轴瓦          Lower half

二十三、主机提交过程用语                               35．电线工         Wireman                    61．推力轴承         Thrust bearing

(Delivery expressions for main engine) 68  36．外包工         Laborer                    62．推力块          Thrust pad

二十四、空压机和空气系统用语                             37．铸工          Molder                     63．推力盘          Thrust disc

(Air compressor and Air system)  ···· 75   38．管子工         Pipe fitter                64．推力轴          Thrust shaft

二十五、锅炉提交用语                                 39．起重工         Crane operator             65．底座           Bed plate

(Delivery expressions for boiler)  ···77   二、柴油机类(Words about diesel engine)         66．机架           Frame

二十 六 、 锚 绞 车 提 交 过 程 用 语 (Delivery   1．主机                   Main engine              67．曲柄箱          Crank case

expressions for anchor windlass)   79      2．二冲程柴油机         Two-stroke diesel engine  68．曲柄箱导门   Crank  case door

二十七、舵机提交过程用语                               3．四冲程柴油机   Fore-stroke diesel engine  69 ．曲柄箱 防爆 门  Explosion-proof  Crank

(Steering gear delivering)  ···    87      4．高速柴油机          High speed diesel engine  case.

二十八、付机提交过程用语                               5 ．中速柴油机             Middle  speed  diesel   70．定时齿轮      Timing gear

（Delivery expression for A/E） ·····  91   engine                                    71．飞轮           Flying wheel

二十九、救生艇提交过程用语                              6．低速柴油机          Low speed diesel engine  72．凸轮           Cam

(Delivery expressions for lifeboat)  ··92  7．气缸盖(缸头)        Cylinder head            73．凸轮轴          Cam shaft

三十、其他提交项目                                  8．安全阀            Safety valve             74．喷油凸轮         Fuel injection cam

(Delivery  expressions  for  other  items)  9．释放阀           Relief valve             75．链条           Chain

···95                                    10．示功阀           Indicator valve          76．链条轮          Chain wheel

三十一、甲板机械系泊试验                               11．示功考克          Indicator cock           77．链条箱          Chain box

(Mooring   test   for   deck   machinery)   12．空气起动阀        Air starting valve       78．推杆           Push rod

········96                               13．起动空气分配器 Air starting distributor  79．摇臂                Rocker arm

三十二、机舱设备系泊试验                               14．油头(燃油喷射器) Fuel injector                80．排气阀          Exhaust valve

(Mooring  test  for  the  equipment  in  E/R)   15．排气阀      Exhaust valve            81．吸气阀           Suction valve

···98                                    16．气缸套           Cylinder liner           82．排气总管         Exhaust manifold

三十三、谈论故障常用语                                17．冷却水套          Cooling water jacket     83．进气总管         Air inlet manifold

（Expressions for trouble） ············100  18．气缸注油器        Cylinder lubricator      84．高压燃油管   High pressure fuel pipe

三十四、谈论检修常用语                                19．活塞            Piston                   85．活塞冷却水管 Piston cooling water pipe

(Expressions for overhaul)  ············ 101  20．活塞头        Piston crown             86．法兰           Flange

三十五、谈论试验和检验                                21．活塞裙           Piston skirt             87．贯穿螺栓         Tie bolt (tie rod)

(Talking    about    test    &     check)  22．活塞销         Piston gudgeon pin         88．端盖           Side cover

···········103                           24．活塞杆         Piston rod                 89．滑油泵          Lubricating oil pump

三十六、谈论技术要求                                 25．活塞环         Piston ring                90．燃油泵          Fuel  oil pump

(Talking about technology required)  ··· 105  26．活塞环槽     Piston ring groove         91．滑油泵齿轮   Gear for lubricating oil

中国船员招聘网http://www.crewcn.com

----------------------- 页面 2-----------------------

中国海员之家网站航海英语系列                                   船  舶  轮  机  英  语  集  成                              第     2   页

pump                                    158．贯穿螺栓             Arrangement of stay

92．燃油泵齿轮  Gear for fuel oil pump        bolt                                     四、阀门(Words about valve)

93．叶轮         Impeller                  159．示功器驱动装置 Indicator driver             1．吸气阀   Suction valve

94．柱塞         Plunger                   160．端罩            End shields           2．排气阀   Exhaust valve

95．导杆         Guide rod                 161．气缸架           Cylinder frame        3．控制阀   Control valve

96．导套         Sleeve                    162．气阀传动装置        Valve operating device  4．导  阀   Pilot valve

97．滚动轴承       Ball bearing              163．摇臂润滑油泵  Rocker arm lubricating  5．单向阀   Non-return valve

98．滑动轴承       Sliding bearing           oil pump                                6．口琴阀   Flap valve

99．推力滚动轴承 Thrust ball bearing           164．摇臂润滑油柜  Rocker arm lubricating  7．调节阀   Regulating valve

100 ．推力面          Thrust  surface  (thrust  tank                                8．液压阀   Hydraulic valve

side)                                   165．摇臂润滑滤器 Rocker arm  lubricating  9．膨胀阀   Expansion valve

101．盘车机       Turning gear              filter                                   10．给水阀  Feed valve

102．增压器       Turbocharger                                                       11．排水阀  Discharge valve

103．涡轮机(透平) Turbine                     三、船舶机械类(Words about marine               12．截止阀  Stop valve

104．涡轮        Turbine wheel                 machinery)                           13．吹泄阀  Blow-off valve

105．涡轮叶片      Turbine blade             1．船用锅炉  Marine boiler                    14．空气阀  Air valve

106．喷嘴        Nozzle                    2．废气锅炉  Exhaust boiler                   15．泄放阀  Drain valve

107．废气叶轮      Exhaust impeller          3．辅锅炉       Donkey boiler                16．止回阀  Check valve

108．废气叶轮片 Exhaust blade                 4．组合式锅炉 Combined boiler                  17．海底阀  Sea valve

109．废气端       Exhaust side              5．火管        Fire tube                    18．回流阀  Retune valve

110．透平端        Turbine side             6．给水管       Feed pipe                    19．节流阀  Throttle valve

111．转子轴        Rotor shaft              7．炉膛        Furnace                     20．进气阀  Inlet valve

112．油泵           L.O.pump               8．炉墙        Furnace wall                21．出气阀  Outlet valve

113．换向装置       Reversing device         9．火侧        Fire side                   22．热力阀  Thermal valve

114．换向伺服期  Reversing servomotor         10．水侧       Water side                  23．中央阀  Center valve

115．压气机(鼓风机) Blower                     11．燃烧器      Oil burner                  24．单向阀  One way valve

116．膨胀接        Expansion joint          12．安全阀      Safety valve                25．二通阀  Two way valve

117．调速器        governor                 13．上排污      Upper drain                 26．三通阀  Triple valve

118．飞重         Flying weight            14．下排污      Lower drain                 27．旁通阀  By-pass valve

119．补偿阀        Compensate valve         15．锅炉皮阀 Mounting valve                  28．换向阀  Change-over valve

120．针阀         Needle valve             16．水位计      Water level gauge           29．减压阀  Pressure-reducing valve

121．开口销        Cotter pin               17．压力表      Pressure gauge              30．溢流阀  Overflow valve

122．轴封         Shaft seal               18．主汽门   Main steam valve               31．自闭阀  Self-locking valve

123．机械密封       Machinery seal           19．玻璃管      Glass tube                  32．针阀      Needle valve

124．配电盘        Switchboard              20．空调装置 Air-conditioning plant          33．平衡阀  Balance valve

125．应急配电盘  Emergency switchboard        21．制冷装置 Refrigerating plant             34．循环阀  Circulation valve

126．应急发电机  Emergency generator          22．冰机          Fridge. Machine          35．主 阀   Main valve

127．滤器         Filter                   23．空气压缩机  Air compressor                36．滑 阀   Slide valve

128．细滤器        Filter                   24．造水机         Fresh water generator    37．蝶 阀   Butter-fly valve

129．粗滤器        Strainer                 25．板式冷却器  Plate type cooler             38．截止阀  Shut-off valve

130．滑油滤器       L.O. filter              26．机舱天车        Engine room crane        39．闸板阀  Gate valve

131．燃油滤器       F.O. filter              27．天车导轨        Crane rail               40．通海阀  Sea suction valve

132．空气消音器        Air intake silencer    28．电磁阀         Solenoid valve           41．吹除阀  Sea chest cleaning valve

132．空气滤器         Air intake filter      29．舵机          Steering gear            42．防浪阀  Storm valve

133．空气瓶          Air bottle (receiver)  30．舵承          Rudder bearing carrier   43．舱壁阀  Bulkhead valve

134．分油机          Separator              31．液压缸         Hydraulic cylinder       44．快关阀  Emergency shut off valve

135．油水分离器        Water-oil separator    32．废气涡轮增压器 Exhaust gas turbocharger   45．呼吸阀  Breather valve

136．净油机          Purifier               33．弹簧阀         Spring loaded valve

137．燃油净化器        F.O. purifier          34．冷凝器         Condenser                五、泵类(Words about pump)

138．二氧化碳         CO2                    35．分油器         Oil separator             1．电动泵  Motor-driven pump

139．二氧化碳瓶        CO2 bottle             36．轴带发电机  Shaft generator               2．柱塞泵  Plunger pump

140．正时齿轮         Timing gear            37．焚烧炉         Oil burner               3．叶片泵  Vane pump

141．导向棒装置        Guide bar              38．分油机         Separator                4．回转泵  Rotary pump

142．注油器驱动        Lubricator driver      39．分离筒         Separator bowl           5．齿轮泵  Gear pump

143．链条张紧装置  Chain tightener             40．配水盘装置  Paring disc device            6．往复泵  Reciprocating pump

144．凸轮轴传动轮  Chain wheel on cam shaft  41．转数计           Revolution counter       7．离心泵  Centrifugal pump

145． 中间链链传动轮 Intermediate chain wheel  42．控制阀          Control valve             1．电动泵  Motor-driven pump

146．注油器驱动装置 Lubricator drive            43．辅机         Auxiliary machinery       2．柱塞泵  Plunger pump

147．链条张紧装置  Chain tightener             44．制冷装置        Refrigerating plant      3．叶片泵  Vane pump

148．滚筒导座         Roller guide housing   45．海水淡化装置 Sea water desalting plant     4．回转泵  Rotary pump

149．应急操纵台        Emergency console      46．热交换器        Heat exchanger           5．齿轮泵  Gear pump

150．力矩平衡器        Moment compensator     47．船用气瓶        Marine air bottle        6．往复泵  Reciprocating pump

151．主启动阀         Main starting valve    48．冷风机         Cooler unit              7．离心泵  Centrifugal pump

152． 启动空气分配器 Starting air distributor  49．防水风门         Fire damper              8．真空泵  Vacuum pump

153．喷油器           Fuel valve            50．气密挡板        Gas tight damper         9．螺杆泵  Screw pump

154．扫气系统          Scavenge air system   51．排气风机        Exhaust fan               10．喷射泵  Ejector pump

155．安全帽           Safety cap            52．舱室通风机   Cabin fan                     11．冷却泵  Cooling pump

156．机座            Bed plate             53．机舱通风机   Engine room fan               12．淡水泵  Fresh water pump

157．轴向振动减振器 Axial vibration damper      54．应急鼓风机   Emergency blower              13．海水泵  Sea water pump

中国船员招聘网http://www.crewcn.com

----------------------- 页面 3-----------------------

中国海员之家网站航海英语系列                                  船  舶  轮  机  英  语  集  成                            第     3   页

14．给水泵  Feed water pump                 11．活络板手  Screw spanner                 81．插头     Electric plug

15．循环泵  Circulating pump                12．梅花板手  Ring spanner                  82．插座     Electric socket.

16．锅炉给水泵  Boiler feed pump              13．呆扳手      Open spanner               93． 喷砂机 Sand blaster outfit

17．卫生水泵  Sanitary pump                  15．套筒板手  Socket spanner                94． 空气马达 Air motor

18．压载泵      Ballast pump                16．管子钳      Pipe spanner               95．油柜清洁器 Tank cleaning machine

19．舱底泵      Bilge pump                  17．螺丝刀      Screw driver               96 ．高压 冲 水 机  High  pressure  hose  for

20．污水泵      Sewage pump                 18．钢丝钳      Wire pliers                hydraulic

21．燃油泵      Fuel pump                   19．尖嘴钳      Long nose pliers           97．真空泵      Vacuum pump

22．高压油泵  High pressure pump            20．钢锯        Hack saw                   98．套筒扳手组 Socket wrench set

23．底压油泵  Low pressure pump             21．剪刀        Scissors                   99． 深头套筒       Deep socket wrench

24．驳运泵      Transfer pump              22．手电筒       Torch                      100．套筒扳手       Box wrench

25．增压泵      Booster pump               23．扁铲(凿子)  Chisel                       101．单开口扳手  Single open end wrench

26．消防泵      Fire pump                  24．锉刀        File                       102．双开口扳手  Double open end wrench

27．通用泵      G.S. pump                  25．丝攻        Thread tap                 103．转矩扳手       Torque wrench

28．旋涡泵      Regenerative               26．板牙        Thread die                 104．电动机扳手  Motor wrench

29．蜗壳泵      Volute pump                27．绞刀        Reamer                     105．侧剪钳        Slide cutting plier

30．导叶泵      Diffuser pump              28．刮刀        Scraper                    106．活节钳        Combination plier

31．单联泵      Simplex pump               29．油石        Oil stone                  107．可调快速扳手 Speed wrench

32．双联泵      Duplex pump                30．拔子(拉马)  Puller                       108．螺丝起子       Screwdriver

33．多联泵      Multiplex pump             31．沙布        Emery cloth                109．偏向螺丝起子 Offset screw

34．活塞泵      Piston pump                32．破布        Rag                        110．六角螺帽起子组 Hexagon nut drivers set

35．减摇泵      Anti-roll pump             33．卷尺        Measuring tape             111．手摇钻        Straight hand drill

36．总用泵      General service pump       34．空心冲       Hole punch                 112．手工锯        Hacksaw frame

37．应急消防泵 Emergency fire pump           35．样冲        Joint punch                113．锯片         Hacksaw blade

38．扫舱泵      Stripping pump             36．油壶        Oil gun                    114．砂纸         Silicon paper

39．货油泵      Cargo oil pump             37．牛油枪       Grease gun                 115．手拉葫芦       Chain block

40．滑油泵      Lubricating oil pump       38．手电钻       Handle drill               116．高压管        High pressure hose

39．钻头        Drill                      117．液压千金顶   Hydraulic jack

六、甲板机械类（Deck machinery）                40．液压千斤  Hydraulic jack.                118．锤子         Hammer

1．锚机       Windlass                    41．塞尺        Feeler gauge               119．平錾         Cold chisel

2．锚机轴      Windlass shaft              42．游标卡尺  Vernier caliper                120．活动扳手       Adjustable wrench

3．刹车带      Brake lining                43．外卡尺       Outside calipers           121．螺丝刀        Screwdriver

4．离合器      Clutch                      44．内卡尺       Inside calipers            122．侧剪铗        Side cutting hipper

5．锚链轮      Anchor Chain wheel          45．螺纹量规 Screw gauge                     123．螺栓剪        Cable cutter

6．轴承瓦      Bearing bush                46．桥规      Bridge gauge                 124．敲击管钳       Rap wrench

7．轴承盖      Bearing cover               47．电焊机  Electrode welding machine       125．砂轮         Grinding wheel

8．绞揽机      Capstan                     48．气焊机  Gas welding machine             126．老虎钳        Utility vise

9．系揽绞车  Mooring winch                  49．电焊钳  Electric welding pliers         127．直梯         Straight ladder

10．卷缆车     Reel                        50．气割枪  Cutting touch                   128．踏梯         Step ladder

11．钢丝绳     Wire rope                   51．电焊条  Electric soldering iron         129．平台推车       Platform trunk

12．卡环      Shackle                     52．电工刀  Electrician knife               130．搬平车        Gas cylinder carrier

13．缆绳      Mooring rope                53．电笔      Test pen                     131．给油机        Grease lubricator

14．滑轮      Block                       54．剥线钳  Wire stripping pliers           132．强力油泵       Heavy duty pump oiler

15．刹车装置 Brake device                   55．圆规      Compass                      133．油壶         Oil jag

16．制链器     Anchor chain stopper        56．量表      Gauge                        134．麻花钻        Twist drill

17．舱盖滚轮 Hatch cover wheel              57．拐档表  Crank deflection gauge          135．绞刀         Pin reamer

18．舱盖铰链 Hatch cover hinge              58．深度规  Depth gauge                     136．旋转中心钻 Rolling center

19．液压油缸 Hydraulic jack                 59．千分表  Micrometer gauge                137 ．外径测微计 Outside micrometer with

20．起货机     Cargo winch                 60．台虎钳  Table vice                           counter

21．可令吊   Crane                         61．柴油      Diesel oil                   138．六折式尺       Six-folding rule

22．生活吊  Accommodation crane            62．滑油      Lubricating oil              139．弹性带尺       Convex rule

23．吊杆      Derrick boom                63．液压油  Hydraulic oil                   140．不锈钢直尺   Stainless steel straight

24．桅杆      Mast                        64．重油      Heavy oil                    rule

25．救生艇  Lifeboat                       65．燃油      Fuel oil                     141．平面规        Surface gauge

26．艇架      Davit                       66．黄油      Grease                       142．平行直角定规 Precision flat try square

27．艇机      Lifeboat capstan            67．螺栓      Bolt                         143．温度计        Thermometer

28．救生筏  Life raft                      68．螺帽      Nut

29．救生衣  Life jacket                    69．垫片      Washer                       八、常用物料(Material in common use)

七、工具类(Word about tools)                70．研磨沙  Grinding sand                   1．阀研磨剂  valve grinding compound

1．车床        Lathe                      71．研磨膏  Grinding paste                  2．电焊条      steel electrode

2．刨床        Planing machine            72．石棉板  Asbestos plate                  3．气焊条      Steel welding wire

3．钻床        Drill machine              73．青壳纸  Fish paper                      4．细钢丝绳  Seizing wire

4．砂轮机       Grinding machine           74．盘根      Packing                      5．刚焊条      Steel welding rod

5．磨床        Grinder                    75．细钢丝  Thin steel wire                 6．紫铜管      Copper tube

6．铣床        Milling machine            76．密封圈  Rubber seal ring                7．乙炔气瓶  Acetylene cylinder

7．镗床        Boring machine             77．塑料管  Plastic pipe                    8．木屑       Saw dust

8．手锤        Engineer’s hammer          78．胶皮管  Rubber hose                     9．水泥       Cement

9．冲击板手      Impact wrench              79．电灯泡  Electric bulb                   10．石灰      Lime

10．板手       Spanner                    80．工作灯  Working lamp                    11．帆布手套 Canvas glove

中国船员招聘网http://www.crewcn.com

----------------------- 页面 4-----------------------

中国海员之家网站航海英语系列                                    船  舶  轮  机  英  语  集  成                              第     4   页

12．垫片       Gasket.                      17．吨          Ton                       4．清洁          Clean

13．氧气瓶      Oxygen cylinder              18．磅          Pound                     5．联接          Connect

14．抹布       Rag                          19．加仑         Gallon                    6．排放压载        Deballast

15．垫隙片      Shim                         20．立方         Cubic                     7．放残水         Drain

16．电线       Wire                                                                 8．卸载          Off

17．电缆       Electric cylinder            十二、国家名称(Name of  country)               9．油漆          Paint

18．电池       Rag                          1．中国       China                         10．接通        Put on

19．灯泡       Bulb                         2．美国       American                      11．吹灰        Soot blown

20．胶布       Insulating tape              3．日本       Japan                         12．开始        Start

21．插头       Plug                         4．英国       Britain                       13．顶端        Top

22．插座       Socket                       5．法国       France                        14．洗         Wash

23．保险丝      Fuse                         6．德国       German                        15．吹         Blow

7．韩国       South Korea                   16．检查        Check

24．不锈钢      Stainless steel              8．希腊       Greece                        17．铲         Chip

25．铸铁       Cast iron                    9．泰国       Thailand                      18．断开        Cut out

26．黄铜       Brass                        10．印度       India                        19．排放        Discharge

27．青铜       Bronze                       11．挪威      Norway                       20．除垢         Descale

28．铝合金      Aluminium alloy              12．俄罗斯      Russia                      21．检验         Examine

29．橡胶       Rubber                       13．新加坡      Singapore                   22．受载         On(load)

30．石棉       Asbestus                     14．澳大利亚 Australia                       23．用泵排出       Pump out

31．低碳钢      Soft steel                   15．伊朗       Iran                        24．调整         Set

32．高碳钢      High-carbon steel            16．丹麦      Denmark                      25．停止         Stop

33．合金钢      Alloy steel                  17．加拿大      Canada                      26．调驳         Transfer

34．木材       Wood                         18．丹麦      Denmark                      27．加满         Top up

35．塑料       Plastic                      19．芬兰       Finland

36．球墨铸铁 Nodular iron                     20．巴基斯坦 Pakistan                        十 六 、 故 障 常 用 单 词          (words  about

21．意大利      Italy                       malfunction)

九、常用紧固件 (Part of fixation in common   十三、常用缩语(abbreviation in common use)   1．失常的                Abnormal

use)                                     1．主机          M/E                       2．烧坏            Burn

1．螺栓           Bolt                      2．付机          A/E                       3．堵塞            Clog

2．螺丝           Screw                     3．阀           V/V                       4．裂缝            Crack

3．螺母           Nut                       4．泵           P/P                       5．变形            Deform

4．方头螺栓         Sq head bolt              5．备车          St/by                     6．毁坏            Destroy

5．埋头螺栓         Counter sunk head screw   6．完车          F.W.E.                    7．磨损            Wear

6．套筒螺栓         Socket head bolt          7．前进三         FAHD                      8．出故障           In trouble

7．定位螺栓         Set screw                 8．微速后退        D.S.Ast                   9．敲击            Knock

8．十字接头         Cross                     9．前进二         H.Ahd                      10．松开          Loose

9．锥形销          Taper pin                 10．高压         H.P.                       11．不对中         Misalign

10．锁紧螺母        Lock nut                  11．低压         L.P.                       12．不足的         Insufficient

11．六角头螺栓  Hex head bolt                  12．重油/柴油       H.O./D.O.                 13．失灵          Out of order

十、常用油类(Oil in common use)                13．前后         F/A                        14．过载          Overload

1．汽油        Gas oil                      14．左舷         P: port                    15．过度磨损        Over-worn

2．煤油        Kerosene                     15．无人机舱       UMS                        16．尺寸过大        Oversized

3．润滑油       Lubricating oil              16．自动         Auto                       17．尺寸过小        Under-sized

4．汽缸油       Cylinder oil                 17．气缸         Cyl                        18．振动          Vibrate

5．压缩机油  Compressor oil                   18．燃油柜        F.O.TK                     19．不平的         Uneven

6．齿轮油       Gear oil                     19．滑油柜        L.O.TK                    20．不准确          Inaccurate

7．机油        Motor oil                    20．沉淀柜        Setl.TK.                  21．全船断电         Black out

8．凡士林       Vaseline                     21．排出         Disc                      22．出故障           Fail

9．燃油        Fuel oil                     22．吸入         Suct                      23．关掉            Shut off

10．油脂       Grease                       23．柴油柜        D.O.TK                    24．弯曲            Bend

11．柴油       Diesel oil                   十四、船用动态常用单词(marine tends word)          25．停车            Break drown

十一、常用量词(Quantifier in common use)        1．停靠       Alongside                    26．腐蚀            Corrode

1． 件，只，个  Piece                          2．接近       Approach                     27．腐蚀的           Corrosive

2． 条，张，片  Sheet                          3．停泊       Berth                        28．损坏            Damage

3． 双           Pair                      4．浮筒       Buoy                         29．有毛病的          Faulty

4． 套，组，副  Set.                           5．码头       Pier                         30．有缺陷的          Defective

5． 盒           Box                       6．港口       Port                         31．破裂            Fracture

6． 箱           Case                      7．移泊       Shift                        32．卡住            Jam

7． 瓶           Bottle                    8．航次       Voyage                       33．漏泄            Leak

8． 米           Meter                     9．试验       Try                          34．漏泄的           Leaky

9． 厘米          Centimeter                10．值班      Watch                        35．融化            Melt

10．毫米          Millimeter                11．航行      Sail                         36．噪声            Noise

11．公斤          Kilogram                                                          37．过热            Overheat

12．克           Gram                      十五、船舶机电设备操作词汇                           38．咬住            Seize

13．公升          Liter                          (manipulate of marine equipment)   39．紧的            Tight

14．平方          Square                    1．调整         Adjust                     40．松的            Loosen

15．袋           Bag                       2．压载         Ballast                    41．发现            Find

16．码           Yard                      3．转换         Change over                42．停止            Stop

中国船员招聘网http://www.crewcn.com

----------------------- 页面 5-----------------------

中国海员之家网站航海英语系列                                      船  舶  轮  机  英  语  集  成                                第     5   页

43．脏的            Dirty                    九十         Ninety                          49．西          West

44．油污的           greasy                   百          Hundred                         50．南          South

45．失效的           ineffective              千          Thousand                        51．北          North

46．椭圆形的          oval                     万          Ten thousand                    52．西北         Northwest

47．点不着火          misfire                  百万         Million                         53．东北         Northeast

48．接错            misjoin                  第一         First                           54．东南         Southeast

49．放错            misplace                 第二         Second                          55．西南         Southwest

50．老化            perish                   第三         Third                           56．世纪         Century

51．麻点            pit                      第四         Fourth

52．凸起            ridge                    第五         Fifth                           二十、常用词组 （Phrases in common use）

53．划伤            score                    第六         Sixth                           1．发现已无法修复  found beyond repair

44

54．拉痕            scuff                    第七         Seventh                         2．发现尺寸过大          found over-sized

第八         Eighth                          3．发现反应缓慢          found slow function

十七、保养检修常用词汇                               第九         Ninth                           4．发现不正常           found out of order

(Words about maintain and examination)   第十      Tenth                           5．发现不合标准         found not up to standard

1．卡死            Blind                     第十一        Eleventh                        6．发现不准确           found inaccurate

2．用卡钳量          Caliper                   第十二        Twelfth                         7．发现失去作用          found out of function

3．关闭            Close                     第二十        Twentieth                       8．发现轧住            found seized

4．解体            Disassemble                                                          9．发现过热            found overheated

5．安装            Fix                       十九、时间、季节与方向                                10．发现过度磨损         found excessive wear

6．组装            Box up                         (Time、Season and Direction)           11．发现过度磨掉         found worn out

7．检验            Check                      1．星期一        Monday                       12 ．发现 有一 点倾斜  found  a  little bit

8．拆卸            Dismantle                 2．星期二          Tuesday                     inclined

9．装配            Fit                       3．星期三         Wednesday                    13．发现不正常          found abnormal

10．紧固           Fasten                    4．星期四          Thursday                    14． 发现因过热而损坏 found destroyed by

11．测量           Gauge                     5．星期五         Friday                                             overheating

12．安装           Install                   6．星期六          Saturday                    15．发现龟裂           found chapped

13．测量           Measure                   7．星期日          Sunday                      16．发现塌陷           found collapsed

14．打开           Open                      8．春季           Spring                      17．发现运转失灵         found out of operation

15．上油漆          Paint                     9．夏季           Summer                      18．发现呈椭圆形         found oval

16．换新           Renew                      10．秋季        Autumn                       19．发现拉痕           found scored

17．上紧           Tighten                    11．冬季        Winter                       20．发现拉毛           found scuffed

18．洗            Wash                       12．一月         January                     21．发现变形           found deformed

19．涂油脂          Grease                     13．二月        February                     22．发现松动           found loose

20．松开           Loosen                     14．三月        March                        23．发现油污           found greasy

21．加油            Oil                       15．四月        April                        24．发现肮脏           found dirty

22．检修            Overhaul                  16．五月        May                          25．发现咬住           found stuck

23．重新组装          Reassemble                17．六月         June                        26．发现挤压           found squeezed

24．测取读数          Take reading              18．七月         July                        27．发现弯曲           found bent

25．拧开螺栓          Unbolt                    19．八月        August                       28．发现故障           found faulty

26．抽出            Withdraw                 20．九月          September                   29．发现损坏           found damaged

21．十月          October                     30．发现破碎成片         found broken to pieces

十八、常用数字(Numeral in common use)            22．十一月         November                    31．发现部分剥离         found partly detached

一       One                               23．十二月         December                    32．发现部分堵塞         found partly choked

二       Two                               24．小时          Hour                        33．发现剧烈震动         found violent vibration

三       Three                             25．分钟          Minute                      34．发现烧坏           found burnt

四       Four                              26．秒           Second                      35．发现断裂           found fractured

五       Five                              27．月           Month                       36．发现接地           found earthed

六       Six                               28．天           Day                         37．发现敲缸           found knocking

七       Seven                             29．夜           Night                       38．发现溶化           found melted away

八       Eight                             30．周           Week                        39 ．发现泄漏             found  leaking  (found

九       Nine                              31．早晨、上午  Morning                          leaky)

十       Ten                               32．下午          Afternoon                   40．发现冻结              found stuck fast by

十一      Eleven                            33．傍晚          Evening                     icing

十二      Twelve                            34．正午          Noon                        41．发现锈蚀           found rusty

十三      Thirteen                          35．今天          Today                       42．发现失效           found ineffective

十四      Fourteen                          36．昨天          Yesterday                   43．发现故障             found out of order

十五      Fifteen                           37．明天          Tomorrow                    44．发现结霜             found frosted

十六      Sixteen                           38．前天          The day before yesterday    45．发现丢失             found lost

十七      Seventeen                         39．后天          The day after tomorrow      46．发现出故障            found in trouble

40．本周          This week                   47．发现失灵             found out of order

十八      Eighteen

41．上周          Last week                   48．发现失灵             found out of  action

十九      Nineteen                          42．下周          Next week                   49．发现不一致           found out of operation

二十      Twenty                                                th

43．九月十日        Sep.10                      50．发现错位             found out of place

三十      Thirty

44．去年          Last year

四十      Forty                             45．明年         Next year                    二十一、常用动词和例句

五十        Fifty                           46．上周二         Last Tuesday                (Verb in common use and example)

六十        Sixty

47．下周一        Next Monday                  1．借    borrow

七十        Seventy                         48．东           East                          我要向你借这份图纸

八十        Eighty

中国船员招聘网http://www.crewcn.com

----------------------- 页面 6-----------------------

中国海员之家网站航海英语系列                                         船  舶  轮  机  英  语  集  成                                   第      6   页

I want to borrow the drawing from you.     20．裂                                            Examine the water seal to see  if there

我可以向你借这个手锤吗?                               二号缸头裂开穿透至冷却水空间                                  is any leakage around the rubber rings.

May I borrow the hammer from you?              No.2 cylinder head is cracked.             检查燃油管。  Examine the fuel oil pipe.

2．裂     break                                21．吊   crane                                 38．制作      fabricate

阀杆断裂了                                         把液压马达吊上岸去修理                                  制作十个活塞销。

The valve spindle is broken.                 Crane  the  hydraulic  motor  ashore  for    Fabricate ten gudgeon pins.

滚动轴承断裂成碎片了                                 repair.                                      39．平顺      fair up

The ball bearing are broken to pieces.     22．割     cut                                     将轴在车床上平顺一下。

3．加强  build up                                   把底座割掉                                      Fair up the spindle on the lathe.

叶轮应该堆焊                                       Cut off the bedplate.                      40．锉       file

The  impeller  should  be  built  up  by  23．损坏  damage                                 原地锉去雷治。

welding.                                         滚动轴承严重损坏                                  File off the ridges on the lathe.

4． 烧     burn                                The ball bearings are seriously damaged.     41．发现      find

电动机烧了 The motor is burnt.                   24．脱落  detach                                 管子发现泄漏。 The pipe is found leaking.

5． 进行  carry out                                 白合金部分脱落了                                 42．刮研      fit and scrape

应进行负载试验                                    The white metal is partly detached.              刮研主轴承轴瓦。

The load test should be carried out.       25．查看      detect                                Fit and scrape the main bearing bushes.

6．吹 blow                                         查看氟里昂系统有无泄漏                              43．回装   fit back

管子必须用压缩空气吹清                                Detect the Freon system for leakage.             所有拆卸的部件修理后装复。

The  pipe  should  be  blown with  compressed  26．解体    disassemble                         Fit  back  all  the  removed  parts  after

air.                                             解体,清洁并检查高压油泵 Disassemble,  repair.

7．铸  cast                                    clean and check the H.P. fuel pump.          44．安装      fix

按原样铸造 一个 Cast  one  piece  as  per  27．脱开            disconnect                             请在这里安装一盏行灯。

sample.                                           把起动空气管脱开                                     Please fix up a portable light here.

8．引起  cause                                  Disconnect the starting air pipe.                喷油器修好后装入气缸盖。

损坏是有剧烈振动引起的 The damage was                  将发 电机与原动机脱开。 Disconnect the                     Fix  the  injector  into  the  cylinder

caused by violent vibration.                 generator from the prime mover.                   cover after repair.

9．倒角  chamfer                                28．讨论       discuss                          45．锻造        forge

油 槽 须 倒 角        Oil  groove  is  to  be   我要和你讨论一下关于主轴承的问题 。                             按原样锻造一个。

chamfered.                                     I  want  to  discuss  with  you  something     Forge  one  piece   according  to  the

法兰切削后须倒角 The flange should be  about the main bearing.                                 sample.

chamfered after being machined.              29．脱开      disengage                             按草图锻造一把专用扳手。

10．换掉  change                                  把联动装置脱开。                                   Forge  a  new  spanner  according  to  the

把它们换掉,否则我拒绝验收                               Disengage the linkage.                     sketch.

Have  them  changed, otherwise  I  refuse  to  盘车机在完成修理工作时需脱开。                            46．折断        fracture

accept them.                                   The turning gear should be disengaged on        锚机右舷机架折断了。

11．龟裂  chap                                  completion of repair work.                        The  starboard  side  frame  of  the

轴瓦上的白合金龟裂了 The white metal on  30．拆卸                dismantle                              windlass is fracture.

the bearing bush is chapped.                   拆卸填料函。                                     47．给         give

12．核查  check                                   Dismantle the stuffing box.                     请 给 我 一 把 板 手 。 Please  give  me  a

用桥规核查主轴承                                   拆卸压缩机。                                     spanner.

Check  the  main  bearing  with  bridge    Dismantle the compressor.                  48．加大黄油  grease

gauge.                                         拆卸一号主轴承上轴瓦。                                    用油脂枪给滚子轴承加大黄油。Grease the

修理前后要核查拐档 Check the crankshaft              Dismantle  the  upper  bush  of  No.1  main  roller bearing with grease gun.

deflection before and after repair.             bearing.                                  49．研磨         grind

13．清洁  clean                                 31．卸下      dismount                              研磨阀与筏座。

装前须清洁  Clean it before fit back.             卸下气缸盖                                          Grind the valve to the seat.

14．阻塞  clog                                    Dismount the cylinder cover.               50．敲          hammer

燃 油 滤 器 阻 塞 了  The  fuel  filter  is  32．做           do                                  请不要这样敲。

clogged.                                         你得重新再做 (返工)。                               Please don’t hammer it this way.

15．涂漆  coat                                      You have to do it all over again.        51．交给         hand over

用红丹涂管子           Coat the pipe with red  33．拉 (拔出)         draw                             测量数据交给轮机长。

lead.                                            将缸套拉出。                                   Please  hand  over  the measuring report  to

泵壳里涂防护漆 The pump casing is to be               Draw out the cylinder liner.             the chief engineer.

coated with anti-fouling.                        柱塞应从导套里拉出。The plunger has to  52．倾斜                  incline

16．完成  complete      finish                  be drawn out from the sleeve.                    活塞有一点倾斜。

你什么时候能完成修理工作?                            34．修饰          dress up                      The piston is a little bit inclined.

When can you complete  (finish) the repair       把轴瓦油路修饰一下。                               53．通知       inform

job?                                             Dress up the oil way of the bush.            当你进行试车时，请通知我。

17．连接  connect                               35．钻           drill                         Please  inform  me  when  you  carry  out  the

把电动机和淡水泵连接起来                                 用手摇钻来钻孔。                                 engine trial.

Connect  the  motor  with  the  fresh  water   Drill it with a hand drill                 54．轧住、咬住 jam

pump                                         36．啮合          engage                            一个活塞咬住在气缸套里。

18．腐蚀  corrode                                   啮合盘车机和飞轮。                                    One   of   the   pistons   jams   in   the

泵壳和叶轮均有腐蚀 The pump casing and  Engage the turning gear with flywheel.                 cylinder.

impeller are corroded.                       37．仔细检查       examine                        55．保持        keep

19．盖     cover                                   把气缸盖送车间检查。Send the cylinder cover            保持通道干净。Keep the passage clean.

请把所有卸下的部件盖起来                             tothe workshop for examination                   保持机舱干净。Keep the engine clean.

Please cover all the removed parts.        检查水封,看看是否在橡皮圈有泄漏。                          56．泄漏      leak

中国船员招聘网http://www.crewcn.com

----------------------- 页面 7-----------------------

中国海员之家网站航海英语系列                                       船  舶  轮  机  英  语  集  成                                 第      7   页

管子因腐蚀而漏了                                    Clean  the  journals  and  prepare  for  Send  the  condenser  to  the  workshop  for

The pipe leaks due to corrosion.        survey.                                    repair.

57．离开      leave                            78．泵  pump                                 95 给…看、出示  show

我们将在本月离开                                    请把污水泵出去。                                   请让我看看如何操作这台机器。

We  are  leaving  this  port  by  the  end  of  Pump out the bilge water, please.      Please show me haw to operate the machine.

this month.                                 79．记录  record                              96．光滑  smooth

58．借（出）  lend                                   请把所有数据记录下来。                                按要求把曲柄销弄光滑。

借一个手电筒给我。                              Record all the readings, please.           Smooth the crankpin as required.

Lend me a flash light.                 80．校正  rectify                             97．准备  stand-by

59．吊   lift out                                 活塞应上床校正。                                   请备车。Stand-by engine, please.

吊一号缸（吊一号活塞）                             The  piston  should  be  rectified  on  the  98．起动、开始  start

Lift out No.1 piston.                   lathe.                                           在起动主机前，我们必须暖缸。

活塞可以用链条葫芦吊出 The piston can  81．调节  regulate                                              We  have  to  warm  the  main  engine

be lifted out by a clean block.                 把空调器的温度调节一下。                           before we start it.

60．闷住   blind                               Regulate   the  temperature  of  the  air-     开泵。Start pumping.

把燃油管闷住进行修理。                             conditioner.                               99．停止  stop

Blind the fuel pipe for repair.         82．修补  remedy                                  停车。Stop the engine.

61借（出）  lend                                    用波浪键修补裂纹。                                  停止泵油。Stop pumping.

借一个手电筒给我 Lend me a flash light.   Remedy the cracks by means of metalock.          100．开、关  switch  (on , off)

62．找  look for                              83．移开  remove                                  请开灯。

你找谁？                                        把活塞杆移开  。                                  Switch on the light, please.

Who are you looking for?                    Remove the piston rod.                     在你离开以前，把灯关掉。

63．旋松  loosen                               84．修补  remedy                                  Switch off the light before you leave.

将螺丝旋松。                                      用波浪键修补裂纹。                              101．告诉  tell

Loosen the screw.                       Remedy the cracks by means of metalock.         请尽快把结果告诉我。

64．加滑油  lubricate                           85．移开  remove                              Tell me the result as soon as possible.

请给轴承加滑油。                                   把活塞杆移开。Remove the piston rod.           102．取（测取）  take

Remember to lubricate the pawls  twice  86．换新  renew                                   把活塞环取出。Take out the piston ring.

every watch.                                     损坏的部件用船上的备件换新。                            测取主轴承压铅丝读数。

65．车  （光车） machine                              Renew the defective parts with ship’s  Take  the  wire  readings  of  all  the  main

把消防泵叶轮耐磨环部位车一下。                         spares.                                    bearings.

Machine the remetall bushes.            87．修理  repair                              103．上紧  tighten

66．熔化  melt                                     我们有一些东西要修理。                                 把气缸盖上的螺母上紧。

白合金已完全熔化了。                              We’ve got something to repair.                 Tighten  up  the  nuts  on  the  cylinder

The white metal has been melted away.       三号辅机去年修过。                              cover.

67．用金属扣和法修 （打波浪键） metalock                  No.3  auxiliary  engine  was  repaired  last  104．拧开  unscrew

裂缝可用金属扣和法修理。                            year.                                           拧开油管接头。

The crack can be metalocked.                88．更换、放置  replace                              Unscrew the oil pipe connection.

68．移动  move                                     用船上的备件更换磨损部件。                          105．使用  use

不要移动那个电动机。                                    Replace   the   worn   out   parts   with   你可以用扳手来松这个螺母。

Don’t move that motor.                    ship’s spare.                                  You  can  use  a  spanner  to  loosen  the

69．测量  measure                                  修理后，备件应放置原处。                           nut.

测量活塞环塔口间隙。                                  The spare parts should be replaced to  106．磨损  wear

Measure  the  thickness  by  means  of  an  the original place after repair.                海水泵叶轮严重单边磨损。

ultrasonic instrument.                          把专用工具放回原处。                                 The impeller of the sea water pump is

70．加滑油  oil                                 Replace the special tools to the original  unevenly worn out.

请 给 轴 承 加 滑 油 。 Oil  the  bearing,  place.                                        107．焊  weld

please.                                     89．上升  rise                                     在增压器焊上一根支撑。

71．打开  open (up)                                冷却水温度突然上升到摄氏 30度。                          Weld   up   one    support   for   the

把气缸盖打开检查。                               The  temperature of cooling water  suddenly  turbocharger.

Open up the cylinder cover for inspection.  rises up to 30℃.                           108．工作 work

72．解体检修  overhaul                           90．转出  roll out                                  发动机不工作了

解体检修主机调速器。                                  把主轴承下轴瓦滚出来。                                  The engine doesn’t work.

Overhaul the main engine governor.      Roll  out  the  lower  half  of  the  main       请抓紧工作。

73．漆  paint                                 bearing.                                         Please  work  against  time.  (seized

阀体内需涂漆。                                 91．运转  run                                 the time please.)

The valve body inside is to be painted.     增压器运转噪声太大                              109．调整  adjust

74．传给、递给  pass                              The  supercharger  runs  with  a  terrible     必需用压铅丝方法调整间隙。

把板手递给我。                                 noise.                                     Clearance  must  be  adjusted  by  means  of

Pass me the spanner.                        92．拉毛  scuff                               lead wire.

75．补、焊补  patch up                               气缸套下部拉毛了                                   把安全阀调整在 0.6 兆帕。

焊补腐蚀部分。                                 The  lower  part  of  the  cylinder  liner  is  Adjust the safety valve to open at 0.6 Mpa.

Patch up the corroded parts by welding.  scuffed.                                      把间隙调整在 0.3毫米至 0.5毫米之间。

76．抛光  polish                               93．咬住  seize                                   Adjust  the  play  between  0.3mm.  and

把主轴颈抛光至镜面。                                  拄塞在导套中咬住了。                             0.5mm.

Polish  the  crosshead  pin  to  mirror  The   plunger   is   seized   in   its   guide  110．同意  agree

surface.                                    (sleeve).                                      我同意你的意见。

77．准备  prepare                              94．送  send                                     I quite agree with you.

清洁轴颈，准备检验。                                  把缸头送到车间去修理。                                我很难同意你的建议。

中国船员招聘网http://www.crewcn.com

----------------------- 页面 8-----------------------

中国海员之家网站航海英语系列                                        船  舶  轮  机  英  语  集  成                                   第      8   页

I can hardly agree to your suggestion.     Approval  of  the  installation  of  fitted  36． 循环滑油预热

111．找中  align                                  bolts.                                      Preheat the circulating pump.

缸套装复后找中气缸(校缸)                            6．中间轴测力验收。                                  37．主机启动试验

Align up the  cylinder after refitting     Approval   of   force   measurement   of      M.E. reversing test.

the liner.原动机和机器对中不良                         intermediate shaft.                         38．应急停车试验

The  prime mover  and  the machine are  7．中间轴承间隙验收                                      Test of emergency stop.

not well aligned.                         Approval  of  the  intermediate  bearing  39．活塞环结胶

112．确认  ascertain                            clearance.                                      Piston ring sticking.

确认所有轴承内滑油供应正常                            8． 中间轴承间隙验收                                 40．滑油老化

Ascertain  the  lube  oil  provision  in  Approval  of  the  intermediate  bearing       Aging of lubricating oil.

all bearing.                            clearance                                   41．早燃

确认无泄漏                                   9． 主机找中不好                                        Pre-ignition.

No leakage is ascertained.                The alignment of M.E. is incorrect        42．调速性能试验

113．叫 & 问  ask                                                                                Governing test.

我可以问你一个问题吗?                              10． 轴系找中不好

68

May I ask you a question?                 The alignment of shafting is incorrect     43．推进特性试验

71

114．组装 & 装配  assemble                        11．曲轴拐档超差                                       Propulsion characteristic test.

备用排气阀应装配好放在安全的地方。                          The  crankshaft  deflection  is  over  the  44．扳紧贯穿螺栓

The  spare  exhaust  valve  should  be  allowance                                       Tighten through bolt.

assembled and kept in a safe place.     12．请调整到范围内                                  45．曲柄臂过长

把倒车机构上的液压伺服器组装好。                             Please make an adjustment .                  The length of crank arm is too large.

Assemble  the  hydraulic  servomotor  of  13．主机外压                                    46．速关阀不灵活

the                                             Outer pressure on M.E.                       Main stop valve isn’t quick.

reversing gear.                          14．主机轴马力                                    47．冷凝器真空度太大

115．变成      become                               The BHP of M.E.                             Condenser vacuum is too large.

十子头销变成椭圆了。                               15．主机扭力                                     48．主机飞车保护试验

The crosshead pin becomes oval.             The tensional force of M.E                   Protection test of  M.E flywheel trip.

这东西(变成)无用了。                              16．主机旁撑                                     49．喷油提前角太大

It become useless                           M．E．side support.                            The advance angle is too large.

116．弯曲      bend                             17．主机尾撑                                     50．喷油嘴雾化不良

这根阀杆有点弯曲。                                   M.E. stern support.                          The atomization of nozzle is too poor.

This spindle is found a bit bent.        18．主机拉撑                                     51．喷油嘴漏油

用加热方法来弯管子。                                 M.E. fastening support.                      The governor has failed.

Bend the pipe by heating it.             19．启动主机                                     52．调速器有故障

Start main engine                            The governor has failed.

二十二、问候和常用表达语                                 20．启动反向。                                    53．快速换向试验

(Greeting and common expression)         Start M.E. reversely                          Quick-reversing test.

1．您好！               How are you！             21．启动往复式内燃机。                                54．翻修期限不清楚

2．见到你很高兴！   I’m glad to meet you!              Start  reciprocating  internal  combustion    Overhaul period isn’t clear.

3．欢迎您到我们船厂来！                                 engine.                                     55．旋转失速

Welcome to our shipyard!   22．柴油机找中不好。                                     Rotating stall.

4．请坐！              Sit down please!            The   alignment   of   diesel   engine   is  56．液压链条压紧装置

5．好的，谢谢！           Thank you!                incorrect                                      Hydraulic chain tightener.

6．早上好，先生！  Good morning sir!                 23．二冲程柴油机。                                  57．缸头启动阀漏气

7．没问题！             No problem!                 The-cycle internal combustion engine.        The cylinder cover starting valve leaks.

8．好的！              Ok!                       24．多种燃料内燃机。                                 58．汽缸油单向阀装反

9．请进。              Yes please.                 Multi-fuel internal combustion engine.       The  cylinder   oil  one-way  valve   is

10．明天见。            See you tomorrow.         25．汽缸工作容积。                                  fitted reversely.

11．我是钳工（电工、工程师）                                Piston displacement.                      59．拉缸       Cylinder score.

I’m a fitter(electrician , engineer).    26． 供油提前角太大。                                60．咬缸       Cylinder seizing.

12．没关系。            Never mind.                 The injection advance angle is too large.  61．敲缸      Cylinder knocking.

13．打扰了。            Excuse me.                27．进行扫气泵扫气。                                 62．燃烧不良         Poor combustion.

14．请多帮忙。           Do me a favour.             Have a blower scavenging.                 63．排气冒黑烟  The exhaust gas is black.

15．现在几点钟？   What time is it?                 28．排气温度太高。                                  64．排气管振动  Exhaust pipe leaks.

16．七点钟。            It ’s seven o’clock.        Exhaust temperature is too high.          65．排气管增加支架

29．启动空气压力低。                                    Attached bracket of exhaust pipe.

二十三、主机提交过程用语                                   The pressure of starting air is too low.  66．排气管支架螺丝未扳紧

(Delivery expressions for main engine)       30．增压器转速低。                                      The  bracket  screw  of  exhaust  pipe  is

1．请验收轴系找中。                                     The rpm of turbocharger is too low.       not tightened.

Please check the alignment of the shafting.  31．调整凸轮间隙。                                  67．冷却水管漏水

2．请验收主机对中。                                     Adjust cam clearance.                       The cooling water pipe leaks.

Please check the alignment of M.E.         32．汽缸间隙太大 。                                 68．油底壳不干净

3．请验收主机曲轴拐挡。                                     Cylinder clearance is too large.          The oil pan is not clean.

Please  check  and  accept  the  crankshaft  33．开启主启动阀                                   69．联焰管联接不紧

deflection.                                    Start the main starting valve.              Cross-ignition tube isn’t tightened.

4．主机联接 （贯穿）螺栓测力验收。                           34．启动辅助风机                                   70．热腐蚀试验

Approval  of  force  measurement  of  M.E.     Start the auxiliary blower.               Accelerated hot corrosion test.

through bolts.                             35．主机暖缸                                     71．主机出油点不畅

5．拂螺栓安装验收。                                       Preheat the M.E cylinder.                 The M.E oil outlets are blocked.

中国船员招聘网http://www.crewcn.com

----------------------- 页面 9-----------------------

中国海员之家网站航海英语系列                                        船  舶  轮  机  英  语  集  成                                   第      9   页

72．主机内部螺丝保险未装好                               12．苛性腐蚀         Alkaline corrosion.          28．起锚试验

The safety of inner screw of M.E is not   13．烘炉        Furnace drying.                   Anchoring test.

fitted property.                           14．煮炉       Boiler out.                      29．加牛油

73．燃油自清滤器不动作                                 15．主蒸气阀提交                                     Add some grease.

The L.O filter doesn’t work.                 Main steam stop valve to be confirmed.     30．请更换压力表

16．燃烧调整试验                                     To renew the pressure gauge.

二十四、空压机和空气系统用语(Air compressor                  Test for combustion control.               31．机座反顶加强

and Air system)                      17．锅炉机动性试验                                    To strength the engine seat.

1．空压机找中提交                                      Boiler maneuvering test.                   32．刹车杆螺丝加油

The   alignment   of   compressor   to   be  18．安全阀调整试验                                   To lubricate the brake threads.

confirmed.                                     Safty valve operation.                     33．离合器加牛油

2．启动氧气压缩机                                                                                  Add some grease to clutch.

Start oxygen compressor.                   二十六、锚绞车提交过程用语                                34．齿轮加牛油

3．直流阀提交                                      (Delivery expressions for anchor windlass)    Add some grease to greases.

The   direct   air-flow   valve   to   be  1．请检查锚机垫片                                    35．更换牛油嘴

confirmed.                                     Please check the windlass washers.          Renew the oil nozzle.

4．排气量超标                                      2．请检查轴系对中                                    36．刹车间隙调整

The amount of free air delivery is more      Please check the alignment of shafting.     To adjust the brake clearance.

the normal.                                3．请检查锚机旁撑                                    37．请检验绞车垫片

5．排气量大                                         Please   check   the   windlass   attacked  Please check the anchor winch washers.

Capacity  at  standard  condition  is  too  bracket.                                    38．绞车轴承间隙

large.                                     4．液压泵压力偏高                                     Anchor winch bearing clearance.

6．排气压力正常                                       The  pressure  of  hydraulic  pump  is  too  39．绞车旁撑

The discharge pressure is normal.          high.                                         Anchor winch attached bracket.

7．主空气瓶密性提交                                   5．油马达压力偏高                                   40．绞车清洁

Gas  tightness  submission  of  main  air    The oil motor pressure is too high.         To clean the anchor winch.

reservoir.                                 6．液压油温度高                                    41．垫片尺寸不对

8．油水分离器提交                                      The hydraulic oil temperature is high.      The washer size is wrong.

The   water-and-oil   separator   to   be  7．冷却水温度高                                    42． 垫片厚度太薄

confirmed.                                   The cooling water temperature is high.      The washer is too thin.

9．无润滑压缩机提交                                   8．锚机清洁                                      43．空载试验

Oil-free compressor to be submitted.        To clean the anchor windlass.                No-load test.

10．日用空气瓶密性试验                                 9．液压泵清洁                                     44．拉力试验

The  gas  tightness  test  of  service  air  To clean the hydraulic pump.                 Pull test.

reservoir.                                   10．请检验油柜                                    45．恒涨力试验

11．日用空气安全阀提交                                   Please inspect the oil tanks.               Constant expansion test.

The   safety   valve   of   service   air  11．试验时间已到                                   46．锚与舷板贴和不好

reservoir.                                      The testing tim is up.                     The anchor doesn’t fit the side plate.

12．应急空压机冲气试验                                 12．有故障                                      47．锚不到位

The   filling   test   of   emergency   air    There’s a failure.                          The anchor hasn’t been lowered enough.

compressor.                                  13．不动作                                      48．手动抛锚

13．水冷式压缩机提交                                    It doesn’t work.                            Manual anchoring.

Water cooled compressor to be confirmed.   14．振动厉害                                     49．机械抛锚

二十五、锅炉提交用语                                     The vibration is violent.                   Mechanical anchoring.

(Delivery expressions for boiler)    15．噪音太大                                      50．轴承温度高

1．主锅炉密性试验                                      The noise is too loud.                      The hydraulic pump is too hot.

The tightness test of main boiler.         16．间隙太大                                      51．液压泵过热

2．制炉       Boiler picking.                     Too much clearance.                         The hydraulic pump is too hot.

3．炉内清洁提交                                     17．负荷太重  Overload.                           52．对中不好

The inside cleanliness to be checked.      18．速度太快         Too fast.                     The alignment is incorrect.

4．锅炉给水泵运转提交                                  19．把液压泵盖打开                                   53．锚未到位

The  running  test  of  boiler  water-feed   Please open the hydraulic pump cover.       The anchor hasn’t been retaken enough.

pump.                                        20．把冷却器拆下                                    54．制链器安装提交

5．给水泵真空试验                                      Please dismantle the cooler.                The  installation of chain stopper to be

The vacuum test of water-feed pump.        21．增加温度表                                    accepted.

6．自动给水提交                                       Add a thermometer.                         55．起锚

The   auto   water-feed   system   to   be  22．增加一个工作台                                   Retake the anchor.

confirmed.                                     Add a working platform.                    56．放锚

7．锅炉蒸发量试验                                                                                  Lower the anchor.

The test of boiler evaporation.            23．增加管子马脚                                    57．收揽

8．炉膛温度过高                                       Add pipe fixed support.  80                 Retake the rope.

The temperature of combustion chamber is  24．请更换液压油                                    58．放缆

too high.                                   Please change hydraulic oil.                Lower the rope.

9 ． 安 全 及 极 限保 护          Safty  and  limit   25．请更换滑油                                    59．蒸气起锚机提交

protection.                                    Please renew L.O.                           Steam windlass to be confirmed.

10．熄火保护  Flame failure safeguard.            26．请放气                                      60．电动起锚机提交

11．蒸汽温度自动调节装置                                  Please discharge air.                       Electrical windlass to be confirmed.

Steam  temperature  automatic  regulating  27．锚机空载试验                                    61．请验收起锚系缆绞盘

system.                                        No load test of anchor windlass.            Please check the anchor capstan.

中国船员招聘网http://www.crewcn.com

----------------------- 页面 10-----------------------

中国海员之家网站航海英语系列                                          船  舶  轮  机  英  语  集  成                                    第      10   页

62．液压起锚系缆绞盘                                   8．舵机安全阀                                        Hand-hydraulic steering gear.

The  hydraulic  anchor  capstan  to  be       Safety valve for steering gear.            42．舵叶舵角限位器

accepted.                                     9．一号缸安全阀                                       Hardover rudder stopper.

63．请验收深水起锚装置                                    Safety valve for No.1 cylinder.            43．操舵轴提交

Please check the deep sea anchor gear.      10．舵压力偏高（低）                                    Steering shafting to be confirmed.

64．启动绞缆机                                        The rudder pressure is too high(low).      44．启动应急操舵索具

Start the warping winch.                    11．跑舵                                          Start emergency steering gear.

65．分链器提交                                        The rudder angle is out of control.        45．板紧舵掣 Tighten the rudder brake

The chain stripper to be accepted.          12．舵压力中心位置                                   46．测量转舵时间

66．锚链轮提交                                        The   position   of   center   of   rudder   Measure the time of rudder movement.

Please check the wildcat and accepted it.  pressure.                                     47．调整最大转舵角度

67．起锚深度是多少米?                                  13．舵杆扭矩偏大                                      Adjust the hard-over angle.

How many metres is heave up depth?            The rudder torque is too large.            二十八、付机提交过程用语

68．系缆速度太慢                                     14．舵高太大                                       （Delivery expression for A/E）

The mooring speed is too slow.                The rudder height is too large.            1． 付机曲拐挡提交。

69．请检验回转吊车绞车                                  15．舵宽太小                                           The   auxiliary    engine    crankshaft

Please check the slewing winch.               The rudder breath is too small.                 deflection to be confirmed.

70．锚抓力是 10kN                                  16．调整初始舵角                                    2． 飞车保护提交。

The holding power-to-weight ratio.            Adjust the initial set rudder angle.         The  protection  of  flywheel  trip  to  be

○

71．链径是 50mm                                   17．舵侧倾角 30                                   confirmed.

○

The chain wire diameter is 50 mm.             The rudder setting angle is 30  .          3． 滑油低压停车提交。

72．放链长度过长  The scope is too long.             18．临界舵角太大                                         The  auto-stop  function  of  L.O.  low

73．锚链转环安全                                       The staling rudder angle is too large.          pressure to be confirmed.

The anchor swivel is safe.                    19．压紧舵杆衬套                                    4． 淡水高温停车提交。

74．螺旋止链器                                        Tighten the rudder stock liner.                 The  auto-stop  function  of  F.W.  high

Screw type chain cable compressor.          20．请检验舵轴                                          temperature to be confirmed.

75．挚链钩提交                                        Please check the rudder spindle.           5． 开始付机负载试验。

The  installation of devil’s claw to be  21．低油位报警                                             Start  the  load  test  of  auxiliary

accepted.                                       Low oil level alarm.                            engine.

76．挚锚链条满足强度要求                                 22．漏油                                        6．调速器突加 （突卸）试验。

Anchor stopper is satisfied to strength.      Oil leakage.                                  Instant load(unload) test of governor.

77．弃链器安装提交                                    23．电动机加润滑油。                                  7． 付机并车试验。

The installation of cable releaser to be      Add some grease to motor.                       The parallel test of auxiliary engine.

confirmed.                                    24．手动操舵                                      8． 超速保护。

78．筒形锚链舱验收成功                                    Manual steering.                                Overspeed protection.

The   submission   of   cylindrical   chain  25．单泵操舵                                           二十九、救生艇提交过程用语

locker is okay.                                 Steering by single pump.                            (Delivery expressions for lifeboat)

79．吊缆锁具安全                                     26．自动操舵                                      1．艇装置提交

The cat tackle is safe.                      Steering by twin pumps.                      Boat   and   boat  handing   gear   to  be

80．请验收导链滚轮                                    27．双泵操舵                                      confirmed.

Please check chain wheel for hawse pipe.      Steering by twin pump.                     2．救生艇立方容量

81．锚浮标提交                                      28．泵组对中提交                                      Cubic capacity of lifeboat.

The anchor buoy to be accepted.               The alignment of pump set to be approved.  3．救生艇乘员定额

82．十字缆桩未固定                                    29．拉杆弯曲                                        Carrying capacity of lifeboat.

The cross bitt isn’t fixed.                   Pull rod bending.                          4．调整救生艇长（艇宽、艇深）

83．系缆穴尺寸偏小                                    30．牛油泵漏油                                     Adjust  the  length  of  lifeboat(the  breath

The size of mooring cup is too small.         Grease pump leakage.                        ,the depth)

84．导缆器提交                                      31．温度表松动                                     5．救生艇总重太重

The fairlead to be confirmed.                 The thermometer is loosened.                 The  total  weight  of  lifeboat  is  too

85．缆绳卷车                                       32．压力表损坏                                     heavy.

Wire reel.                                    The pressure gauge is damaged.             6．增加救生艇内部浮力

○         ○

33． 0 到左舷 35                                   Increase the inherent buoyancy.

○

二十七、舵机提交过程用语                                    Nil to port 35 .                           7．划浆救生艇提交

○         ○

(Steering gear delivering)            34．右舷 35 到左舷 35                                Oar-propelled lifeboat to be accepted.

○           ○

1．请检验舵机垫片                                       Starboard 35  to port 35 .                 8．人力机械推力救生艇

Please  check  the  washers  of  steering                                                  Manually mechanically propelled.

gear.                                         35．主动转向装置                                    9．联动脱钩装置

2．请检查辅助操舵装置                                   Activated maneuvering device.                  Simultaneous disengaging gear.

Please check the auxiliary steering gear.  36．侧向推力器提交                                    10．救生衣         Lifejacket

3．请检验舵机旁撑                                       Transverse thruster to be accepted.        11．吊艇架提交

Please  check  the   steering  gear   side  37．主动舵验收                                      Boat davit to be confirmed.

bracket.                                        Active rudder to be accepted.              12．吊艇架额定负荷

4．舵机安装尺寸                                      38．可转推力器                                       Loading capacity of boat davit.

The installation size of steering gear.       Retractable steering thruster.             13．修改降落时限

5．请检验应急操舵装置                                   39．舵链传动操舵装置                                    Change the time limit to launch.

Please check the jury steering gear.          Chain barrel steering gear.                14．降低安全降落速度

6．中舵       Centerline rudder .                40．螺杆传动操舵装置                                    Reduce the safety falling velocity.

7．舵机零位                                          Screw steering gear.                       15．救生艇属具

Nil position of steering gear.              41．人力液压操舵装置                                    Equipment of lifeboat.

中国船员招聘网http://www.crewcn.com

----------------------- 页面 11-----------------------

中国海员之家网站航海英语系列                                         船  舶  轮  机  英  语  集  成                                   第     11   页

16．艇架强度试验                                      The chain runs well in the hawse pipe.     16． 扫气箱高温降速

The strength test for davit.               6．锚链与止链器啮合良好                                  Scavenging  box  high  temperature  slow-

17．救生艇强度试验                                     The chain engages the chain stopper well.  down.

The strength test fore life-boat.          7．试验情况良好，同意验收。                               17．推力轴承滑油温度

18．收艇       Boat retaking.                     The test is okay and it can be accepted.    Thrust bearing L.O. temperature.

19．放艇       Boat lowing.                     8．固定锚卸扣                                      15推力块滑油高温报警

20．自动脱钩                                        To fix the anchor shackle.                  Thrust block L.O. high-temp alarm.

Unhook automatically.                      9．增加锚链径                                      16 正车（倒车）1小时

21．再做一次                                        Reel back the anchor lashings.              Ahead (Astern) for 1 hour.

Do it once again.                          10．导链滚轮工作正常                                  18．各缸工作参数

22．电器限位不好                                      The  chain  wheel  for  hawse  pipe  works  Working parameters for each cylinder.

The  limiting  switch  of  the  appliance  formals.                                    19．主机航行试验

doesn’t work.                             11．锚链拉断试验                                     Main engine portion of trial test.

23．请动车                                          Breaking test for anchor.                三十三、谈论故障常用语 （Expressions for

Please start.                              12．这个缆绳测力计准确吗？                              trouble）

24．艇架反顶加强                                       How  about  the  accuracy  of  the  cable   1．电动机出了什么故障？

Strengthen the davit from underside.         tension indicator?                        What’s wrong with the motor?

25．起艇机二级启动不好                                 13．舱口盖绞车收放试验                                2．绞盘出了故障。

The  two-stage  boat  lifer  doesn’t  start    The operating test for hatch cover winch.  There   are   something  trouble  with  the

successfully.                                14．回转试验         Turning circle test.        capstan.

26．保险杆不活络                                    15．同时用 1号、2 号泵                              3．泵的叶片严重损坏。

The safety lever is not flexible.            Run No.1 and No.2 main pumps.             The blade of pump are badly burnt.

27．修整                                        16．检查安全装置                                   4．风机振动的厉害。

Make an adjustment.                          To check the safety device.                   The fan blower vibrates violently.

28．轴封漏油                                      17．空载试验         Idle running.               5．The valve spindle is bent and twisted,

Shaft tunnel oil leakage.                  18．变幅试验         Luffing test.               because it is misaligned.

19．试验刹车性能                                         阀轴弯曲且摇摆，因为未对中。

三十、其他提交项目                                       The brake performance test.              6．There are very corrosion on blade.

(Delivery expressions for other items)       20．吊不起 50 吨                                       叶片腐蚀严重。

1．泵真空提交                                         It can’t life up the weight of 50T.      7．We measure the temperature of the motor.

The vacuum of pump to be confirmed.        21．倾斜试验        Tilting test.                      我们测量了电机的温度。

2．泵压力提交                                      22 空载试验       No-load test.                 8．The pump had cracked beyond repair.

The pressure of pump to be confirmed.      23试验误差较大，再做一次。                                    泵损坏的已经失修了。

3．泵自动转换提交                                      The error for the test are too many, do  9．Where is the pump located?

The auto-shafting function of pumps to be  it again.                                           泵在哪儿？

confirmed.                                   三十二、机舱设备系泊试验                                 10 ． Is  it  because  the  shaft  aren’t

4．燃油分离机效用提交                                  (Mooring test for the equipment in E/R)     properly positioned?

The effect test of D.O purifier.           1．设备安装检查                                          是不是轴没有安装好？

5．仓库水分离器效用提交                                   To check the equipment installation.       11 ． There  are  on  the  central  control

The effect test of L.O. purifier.          2．舱底泵压力检查                                   console.

6．焚烧炉效用提交                                      To check the pressure of bilge pump.            在中央控制台上。

The effect test of incinerater.             3．锅炉给水泵效用试验                                 三十四、谈论检修常用语

7．鼓风机运转提交                                      The test of boiler feed pump.                      (Expressions for overhaul)

The running test of blower.                  4．锅炉及相关系统检查                                  1 ． Would  you  please  inspect  the  main

8．蒸气管畅通试验                                      To check the installation of boiler and  engine?

The running test of vapor pipes.             its accessories.                              能检查一下主机吗？

9．柴油分离机效用提交                                  5．燃油器断开                                     2．Make an overall check of the winch.

The effect test of fuel separator.           To cut-off the burner.                          对绞盘全面检查。

10．水密滑门速闭装置                                  6．自动给水试验                                    3 ． Check  the  gap  of  brake  facing  both

Quick-closing   controlling   gear    for    Automatic change-over test.               before and

sliding door.                                7．废气燃油交替式锅炉                                  after repair.

11．海水蒸发器提交                                     Alternatively-fired exhaust gas boiler.     在维修前后都要检查制动衬片的间隙。

The sea water evaporator to be confirmed.  8．废气燃油组合式锅炉                                 4．It is necessary to examine the pump.

三十一、甲板机械系泊试验                                   Composite oil-exhaust gas fired boiler.     有必要检查这台泵。

(Mooring test for deck machinery)      9．主空压机系泊试验                                  5．The ball bearing should be pulled out

1．设备安装完整性良好                                    Mooring test for main air compressor.       for examination.

The   installation   of   equipment    is  10．充气试验                                       滚珠轴承应该拿出来检测。

finished.                                      Air charging test.                        6．Leave a mark here.     做个标记。

2．空卷筒正向运转 5分钟                                11．检查排气量                                    7．Cutting a hole here.

Keep  the  gypsy  running   idle  for  5     To check the free air capacity.             在这儿开个洞。

minutes                                    12．通风系统                                     8．It should be replaced by a new one.

positively.                                 The   installation   of   air  ventilation  应该换新的。

3．检查轴承发热状况                                     system.                                   9．Machine the surface.

To  check  the  hot  condition  of  the   13．负荷限制功能试验                                    加工平面。

bearing.                                       Load-limit function test.                  10．Replace it with a new one.

4．左锚机机械抛锚                                    14．启动空气管吹洗                                    换新。

Mechanical   anchoring   for   the   port    Blowing-off of the starting air pipe.      11．Big clearance of the brake facing.

windlass.                                    15．启动换向试验                                     制动衬片间隙大。

5．锚链在锚链筒内运行良好                                  Change-over starting test.                 12．Round the edges.

中国船员招聘网http://www.crewcn.com

----------------------- 页面 12-----------------------

中国海员之家网站航海英语系列                                             船  舶  轮  机  英  语  集  成                                        第      12   页

加工外圆。                                         brushed.                                         assembly  n. 装配

13．Returned to the ship as spare part.             水柜除锈并用钢丝刷刷净。                                  astern  n. 倒车

作为备件返还船上。                                                                                      atmospheric survey 大气环流调查

14．There is no need to change it.                                                                atomic power 原子能

不用更换。                                                                                          atomize v. 雾化

VOCABULARY                       authority  n. 当局

三十五、谈论试验和检验                                     3-roller bending machine 三 弯机                    automatic control device  自动控制装置

(Talking about test & check)           abandon v. 弃船                                    automatic production line  自动生产线

1．Please carry out the protection tests on  abolish v.  消除                                       automatic steering  自动操舵

board.                                          ABS   美国船级社                                      automatic submerged arcwelding  自动埋弧焊

请在甲板上做保护试验。                                   acceleration   n. 加速度                            automatic telephone  自动电话

2．The steering gear has been repaired. We  accelerometer   n. 加速度表                               aux. boiler 副锅炉

are going to try it.                            accommodate  v. 容纳                               aux. engine 辅机

操舵装置已经修好了。我们打算试一试。                            accommodation deck                               aux. engineroom 辅机舱

3．Don’t switch on.                              起居(住舱)甲板                                         aux. machinery 辅机

不要接通。                                         accuracy   n. 精度                                 auxiliary means 辅助手段

4．Don’t switch off.                             accurate synchro device 准同步装置                    auxiliary system 辅助系统

不要关上。                                         acetylene cutter 气割机                             axial push 轴向推力

5．Turn on the light.                            acid-pickling   n. 酸洗                            backing  n. 衬垫

打开灯。                                          acoustics  n. 音响效果                               ballast piping 压载水管系

6．Turn off the light.       关上灯。                adhesiveness  n. 粘附力                             ballast pump 压载泵

7．There is still a crack here. Please have  adjacent  a.相邻的                                      ballast system 压载系统

it welded up.                                   adjust v. 调节                                     ballast water  压载水

这儿仍有个裂缝。请焊接上。                                 administration  n. 行政管理                          base  n. 基准

8．Please give me a survey report.               admit v. 接纳                                      basepoint  n. 基准点

请给我一个测量报告。                                    adopt v. 采纳，采用                                   basic design 基本（方案）设计

9．Let me see the relevant drawing.              affiliated factory  分厂，附属工厂                      basic metal 母材

让我看看相关图纸。                                    aforementioned  a.前述                             battery unit 蓄电池组

10．These screw are loose. They should be  aft  a. adv.  n.  （在）船艉                                beam  n. 波束

tighted.                                        aftpeak 艉尖舱                                      beam  n. 横梁

螺丝钉松了，需紧一下。                                  after service 售后服务                               bearing  n. 轴承

10．May I use the ladder for a moment.           ahead  n. 正车                                     bearing hole  n. 轴承孔

我可以用一下梯子吗？                                   airbottle  空气瓶                                   bedplate  n. 机座

11．Is it all right like this?                   aircompressor  空压机                               bell set 铃组

像这样好了吗？                                      airreservoir 气瓶                                  bending machine 冷弯机

airsiren 汽笛                                      berth  n. (水平)船台，（船上）床铺

三十六、谈论技术要求                                      air-tight test 气密实验                              berth or slipwayfabrication

(Talking about technology required)             alarmbell 警铃                                     船台装配

1．All parts to be reassembled as original.  alignment  n. 找中                                     bilge  n. 舱底水

所有部件按原样组装。                                    allwaves 全波                                      bilgekeel 舭龙骨

2 ． Ring  grooves  to  be  machined  up  as  allowance  n. 允值                                    bilgeplate 舭板

original.                                       allposition 全方位                                  bilgepump 舱底水泵

环槽按原尺寸加工。                                     alternating current (A.C.) 交流电                   bilgesystem 舱底水系统

3．Valve spindle to be remade according to  ammonia  n. 氨                                         binarysystem 二进位制

the drawing                                   amplifyv. 放大                                     blank  n. 毛胚

阀杆按图样新做。                                      anautomatic production line                      block  n. 分段

4．One cylinder liner to be newly made as   自动生产线                                                 block or section fabrication

analogous output 模拟输出                            分段或总段装配

spare.

新做一缸套作为备件。                                    analogue computer 模拟计算机                          blood vessel 血管

5 ． Shaft  to  be  lathed  as  per  attacked  anchor  n. 锚                                       blower 风机

sketch.                                         anchor chain  （cable chain）锚链                    bluecollar worker 蓝领,工人

轴按附图加工。                                       anchor handling 锚操纵                              boat deck 艇甲板

6．Cylinder liner to be tested as required.  anchor windlass (chain windlass)                     bollard  n. 带缆桩

7．Coupling to be bored as required.             起锚机                                              bolt  n. 螺栓

联轴节在轴的部位光车。                                   anchorage buoy 系泊浮筒                              bolthead  n. 螺栓头

8．Crankpins to be polished in place.            angular  n. 角度                                   bottom  n. 船底

曲柄销就地抛光。                                     antenna  n. 天线                                   bottom plate 底板

9．Cylinder to be hydraulically tested in  anticorrosion precaution  防腐措施                         bottom structure 底板结构

face of C/E and surveyor.                       apparatus  n. (pl. apparatus or apparatuses)     bow  n. 船艏

气缸需在轮机长和验船师在场时进行液压试验。                            仪器，器械，装置                                        bow &sternstructure 艏艉结构

10．Cooling system to be tested to C/E’s  appearance  n. 外观                                       bow section 艏段

satisfaction.                                   approval  n. 批准，认可                               branch company 分公司，子公司

冷却系统试验至轮机长满意为止。                               approve  vt. 认可                                  branch system 分系统

11．Clearance to be measured with a feeler.  arbitrate v. 仲裁                                      bridge  n. 桥楼

间隙用塞尺检查。                                      arc  n. 弧度                                       bridgecontrol 桥楼控制

12 ． Packing  to  be  renewed  with  ship’s  arduous  a.艰难的                                      broadcast  n. v.  广播

store.                                          arrange v.  布置，安排                                broadcast station 广播站

填料用船方备件换新。                                    asbestos  n. 石棉                                  bronze sleeve 青铜套筒

13.Water  tank  to  be  de-rusted  and  wire-  assemble v. 装配                                    bulbous bow 球鼻艏

AssembleLanguage 汇编语言

中国船员招聘网http://www.crewcn.com

----------------------- 页面 13-----------------------

中国海员之家网站航海英语系列                                                船  舶  轮  机  英  语  集  成                                           第       13   页

bulk cargo 散装货物                                    compartment stuffing box                           deadweight ton(DWT)  n. 载重量，吨载量

bulk-cargo carrier 散装货船                            隔舱填料函                                              Decca receiver  台卡定位仪

bulkhead  n. 隔舱壁                                   compass  n. 罗经                                     deck  n. 甲板

bulkhead structure 隔舱壁结构                           compass deck  罗经甲板                                 deck girder  甲板材

bushing  n. 衬垫                                     compensate  vt. 补偿                                 deck longitudinal  甲板纵骨

butt joint 对接接头                                    competition  n. 竞争                                 deck machinery  甲板机

cabin  n. 舱室                                       completion drawing 完工图                             deck plate  甲板板

cablefixture 电缆夹具                                  component  n. 组成部分                                 deck structure  甲板结构

calculation  n. 计算                                 composition  n. 成分组成                               deckhouse  甲板室

calculator  n. 计算器                                 compound excitation 复励                             deform v.  形变

calibratev.  校正                                    comprehensiveproductivity 综合生产能力                   deliver v.  交货，交船

calibration  n. 校正                                 compressed air 压缩空气                                delivery  n. 交船，交货

cam  n. 凸轮                                         compression (power)stroke  n. 压缩冲程                 delivery ceremony 交船典礼

cam follower  凸轮附件                                 computer control console 计算机控制台                    derrick  n. 吊杆

camber  n. 梁拱                                      conceptual  a. 概念的                                 designstage 设计阶段

camshaft  n. 凸轮轴                                   condensation  n. 冷凝                                designation  n. 名称，牌号

capstanwindlass （anchor winch）                     conductor  n. 导体                                   designation  n.  目的地

锚绞盘                                                connecting rod 连杆                                  detail design 详细（施工）设计

cargo  n. 船货                                       connection  n. 接头                                  detect v.  探测

cargo oil 货油                                       constant voltage 恒压                                detect v.  侦察

cargo –hold  n. 货舱                                 constitutev.  构成                                   detection  n. 探测

cargo-lifting  n. 起货                               consumables  n. 消耗品                                deviation  n. 位移

casing  n. 罩壳                                      consumption  n. 消耗                                 dial  n. 刻度盘

cast iron piece 铸铁件                                contact v.  触发                                     diameter  n. 直径

casting  n. 铸造                                     container  n. 集装箱                                  differentia  n. 差异

cathode-ray type 阴极射线式                             continuous deck 连续甲板                               digital computer 数字计算机

CCS 中国船级社                                          contract  n. 合同                                    digital output 数字输出

central control 集控                                 contradiction  n. 矛盾                               direct current(D.C.)直流电

centreline  n. 中心线                                 control component 控制元件                             direct drive 直接传动

centrifugal  a.离心的                                 control console 控制台                                direct telephone 对讲电话，直线电话

certificate  n. 证书                                 control unit 控制装置                                  directional finder 测向仪

chain drive 链传动                                    converse method 反装法                                directional instrument 指向仪器

chain locker 锚链舱                                   convertor  n. 转换器                                  directional stability 航向稳定性

chain pipe 锚链管                                     conveyor  n. 传送带                                   disc  n. 圆盘

chain reaction 连锁反应                                coolant  n. 致冷剂                                    discharge  n. v.  排水

chain stopper 制链器                                  coolant(cooling agent)n. 制冷剂                       dispensable  a. 非必要的

challenge  n. v.  挑战                               cooler  n. 冷却器                                     dispute  n. v.  争端，争执

chamfer v.  在边缘切斜面                                 cooling system 冷却系统                                distributev.  分布

changeover switch 转换开关                             cooperation  n. 合作                                 distributev.  分配，配电

characteristics  n.                                coordinate  n. 坐标                                  distribution  n. 配电

性能，特性，特征                                           coreenterprise 核心企业                                distribution box 分电箱

chargev.  充（电，气）                                   corrosion  n. 腐蚀                                   distribution panel 区配电板

check  n. v.  检验                                   corrugated  a. 波纹状的                                distribution switch 配电开关

chemical medium 化学介质                               course  n. 航向                                      distribution system  n. 配电系统

China Classification Society(CCS)                  cover  n. 药皮                                       division  n. 划分

中国船级社                                              CPP drive 可调浆传动                                    DNV 挪威船级社

China OceanShipping Company (COSCO)                crank cheek  曲柄夹板                                  Dock  n. 船坞

中国远洋公司                                             crankcase  n. 曲柄箱                                  dock trial  码头试验

chip  n. 芯片                                        crankpin  n. 曲柄臂                                   docking winch 带缆绞车

circle  n. 圈子，团体                                   crankshaft  n. 曲轴                                  Doppler effect 多普勒效应

class  n. 船级                                       crankweb  n. 曲柄臂                                   Doppler frequency offset 多普勒频移

classification  n. 船级                              crew  n. (全体)船员                                    Doppler sonar log

classification society 船级社                         cross section 截面                                   多普勒声纳计程仪

cleanness  n. 清洁度                                  crosshead  n. 十字头                                  doublebottom 双层底

closed circulation  闭式循环                           cultivatev.  培养，培育                                 double-action  a.双作用

clutch  n. 离合器                                     current  n. 电流                                     down-vertical welding 下行焊

CO2shielded arcwelding 二氧化碳气体保护焊                   current  n. 洋流，水流                                  draft(draught)n. 吃水

Coating  n. 图层                                     current-impulse frequency convertor                drainage  n. 疏水，泄水

code  n. 法典                                        电流-脉冲频率变换器                                         drawing  n. 图纸

codedisplay circuit 编码显示电路                         curve  n. 曲线                                       drawing instrument 绘图仪

coefficients of ship form 船型系数                     cutting  n. 切割                                     drift v. 漂移

cold processing 冷加工                                cylinder  n. 气缸                                    drinking water 饮用水

collision  n. (船只)碰撞                               cylinder block 气缸体                                 drip-proof type 防滴式

combustibility  n. 可燃性                             cylinder cover (cylinder head) 缸盖                  drive  n. 传动

combustion  n. 燃烧                                  cylinder liner 气缸衬套                                drivemechanism 传动机构

combustion chamber 燃烧室                             cylinder oil 气缸油                                   drivemechanism 传动装置

combustion gas 燃气                                  cylinder wall 缸壁                                   driveunit 传动装置

commanding telephone 指挥电话                          data impulse 数据脉冲                                  driven shaft 从动轴

communication  n. 通讯                               davit  n. 吊艇架                                      dry v.  烘干

compartment  n. 分隔舱

中国船员招聘网http://www.crewcn.com

----------------------- 页面 14-----------------------

中国海员之家网站航海英语系列                                                 船  舶  轮  机  英  语  集  成                                           第       14   页

drydock  n. 干船坞                                    excitev.  激励                                       Freon  n. 氟利昂

dynamic –pressuretype 水压式                          exhaust port 排气口                                   frequency  n. 频率

echo signal 返回信号                                   exhaust stroke 排气冲程                                frequency difference latching

echo sounder  回声测深仪                                exhaust valve 排气阀                                  频率锁定

economic effect 经济效益                               expand v. 扩张，扩建                                    frequency regulation 调频

edgepreparation 边缘加工                               expansion  n. 展开图                                  fresh water  （F.W.）淡水

edgeprocessing 边缘加工                                expansion stroke 膨胀（作工）冲程                          fresh water production plant

edger  n. 刨边机                                      expansion tank 膨胀箱                                 造水装置

eject v.  喷射                                       experiment  n. 实验                                  friction resistance 摩擦阻力

elapse v.  （时光）消逝                                  exterior force 外力                                  fuel  n. 燃料  fuel nozzle 喷油嘴

electric brain  电脑                                 extinguish v.  灭火                                  fuel oil 燃油

electric load 负荷                                   F.O.meter 燃油流量计                                    fuel oil  （F.O.）燃油

electrical arc  电弧                                 F.O．tank 燃油舱                                       fuel pipeline 燃油管系

electrical compass  电罗经                            Fabricatev.  装配，制作                                 full-load  a. 满载的

electrical drive  电力托动                             fabrication  n. 装配                                 full-load displacement 满载排水量

electrical energy  电能                              facileadaptability 灵活的适应性                          funnel  n. 烟囱   galley  n. 厨房

electrical impulse  电脉冲                            facsimile transmission(fax)传真                      gantry  n. 龙门架  gas cutting 气割

electrical power  电力                               fairing  n. 光顺体，流线体                                gas tight seal 气密密封

electrical shedding 放电                             fair-lead  n. 导缆孔                                  gas turbineengine 燃气轮机

electrical signal  电器信号                            fashioned steel 型钢                                 gas welding 气焊  gear  n. 齿轮

electrical slag welding  电焊渣                       fast speed (rapidity)快速性                           gear drive 齿轮转动

electrical unit  电器装置                              fathometer  n. 侧深仪                                 geo-physical propecting vessel

electrical user  电器设备                              feed v.  馈给                                        地球物理探测船

electrical-driven  a. 电动的                          feed circuit 馈电线路                                  GL 西德劳氏船级社

electrician  n. 电工                                 fillet seam 角焊缝                                    grant v.  给予……的权利

electricity  outfitting  电舾                        fillet welding 角焊                                  gravitycentre 重心

electrode  n. 焊条                                   filter  n. 过滤器. 过滤                                 gravitywelding 重力焊

electromagnetic contactor  电磁接触器                   fine  a. 纤细的                                       groovev. 开坡口  ground v.  接地

electromagnetic induction  电磁感应                    finished product 成品                                group  n. (企业)集团

electromagnetic log  电磁计程仪                         firealarm 火警                                       growth  n. 生长，发育

electromagnetic sensor  电磁传感器                      firehazard 火灾                                      guarantee  n. v.  保证

electronic computer  电子计算机                         firepump 消防泵                                       general description 概述

electronics  n. 电子（学）                              fire-fighting system 消防系统                          general-purpose  a.通用的

element  n. 机械零件                                   fire-resistant  a.耐火的                              generating set 发电机组

element  n. 要素                                     fixed part 固定件                                     geometrical characteristics 几何特征

emerge v.  崛起，兴起                                   flash signal light  闪光信号灯                          geometrical principle 几何原理

emergency control 应急控制                             flat fillet seam 平角焊缝                              gravity launching 重力下水

emergency network 应急电网                             flexibility  n. 挠性                                 guided-missile frigate 导弹护卫舰

emergency power station 应急电站                       flexiblecoupling 挠性联轴节                             gyro  n. 陀螺仪

emergency radio transmitter                        float launching 漂浮下水                               gyro compass  陀螺罗经，回转罗经

应急无线电发信机                                           floatability  n. 漂浮性                               H.D.HeavyMachinery Co. Ltd. H.D.

emergency steering 应急操舵                            floating positively 正浮                             重机股份有限公司

emergency switchboard 应急配电板                        floating production storage unit(FPSU)             Halogen  n. 卤素

emergency telegraph 应急传令钟                          浮式生产储油轮                                            hand control 手控  hand level 手柄

emergent discharge 应急排放                            flood v.  进水                                       hand steering 手动操作

emergent service 应急使用                              floodability  n. 不沉性                               hand wheel 手轮   handlev. 操纵

enclosev.  封闭                                      floor plate 肋板                                     harbour  n. 港口，停泊

encounter v.  遭遇                                   fluctuatev.  波动                                    harbour generator 停泊发电机

energyconvertor 换能器                                fluctuation  n. 波动                                 hardware  n. 硬件

enginefoundation (engineseat )机座                   flush v. 清洗                                        hatch trunk 舱口围壁

engineframe 机架                                     flushing agent 清洗剂                                 hawsepipe  n. 锚链筒

engineoil 机油                                       flux  n. 焊剂                                        hewater pressure system 水压系统

engineoutfitting 机舾                                flywheel n 飞轮                                      headquarters  n. 总部，厂部

enginespace 机舱                                     foam  n. 泡沫                                        headroom  n. 甲板间高度

engineer  n. 轮机员                                   folding machine 折边机                                heat exchanger 热交换器

engineer  n. 工程师                                   for home use 国内用                                   heating  n. 供暖

engineering andtechnical team                      forced lubrication 强制润滑                            heavy current  n. 强电

工程技术队伍                                             forced ventilation 机械通风                            heavy oil 重油  heel  n. 横倾

engineer vessel 工程船                                foreperpendicular 艏垂线                              hereinbelow adv.  在下文

engine-room 机舱                                     forecastle  n. 艏楼                                  high frequency 高频

ensurev.  确保                                       foreign trade 外贸                                   high-speed boat 高速艇

enterprise  n. 企业                                  forging  n. 锻造                                     horizontal  a.水平的，卧式的

EO 无人机舱                                            formation  n. 构成，结构                                horsepower(hp)  n. 马力

equipment  n. 设备                                   frame  n. 肋骨                                       hose  n. 软管

error  n. 误差                                       framework  n. 框架                                   hot processing 热加工

essence  n. 实质，本质                                  framing block 肋骨框架分段                               hot work 火工  hull  n. 船体

evolvev.  渐进，进化，演变                                 freeend  自由端                                       hull cleanness 船体光顺性

excessive  a. 过量的，极度的                              freeboard  n. 干舷                                   hull construction  船体结构

excitation  n. 励磁                                  freighter  n. 货船                                   hull form 船型   hull line 船体线型

hull structure 船体结构

中国船员招聘网http://www.crewcn.com

----------------------- 页面 15-----------------------

中国海员之家网站航海英语系列                                                船  舶  轮  机  英  语  集  成                                            第       15   页

human brain 人脑  humidify v. 增湿                      life-or-death  a.生死攸关的                             manual work 手工劳动

hydraulic  a. 液压的                                   life-raft  n. 救生筏                                  manufacture  n.&v.  生产，制造

hydraulic fluid 液压流体                                life-saving  n. 救生                                 marinecrane 船用起重机

hydraulic machine 液压机                               lifting capacity 起重能力                              marinediesel engine 船用柴油机

hyperbolic curvereceive 双曲线定位仪                      light current 弱电   lighting  n. 照明                 marineengineer 机电工程师

identify  vt.识别                                     light-ship displacement (light-load displacement)轻  marineengineering research institute

ignitev. 点火   ignition  n. 点火                       载排水量                                               造机研究所

illumination  n. 照明                                 lines lofting 线型放样                                 marinegeological research vessel

illustration  n. 生动的说                               lines offsets 型值                                   海洋地质调查船

imagedisplay system  图象显示系统                         lines plan 线型图  lining  n. 衬垫                      mark v. 标出

IMCO 政府间海事协商组织                                      load distribution 负荷分配                             mast light

impact  n. 冲击  implication  n. 含义                   load linemark 载重线标志                                master controller 主令控制器

impulsator  n. 推动器，脉冲发生器                            load transfer 负荷转移                                 Master degree 硕士学位

impulse-type  a.脉冲式的                                local strengthening 局部加强                           material  n. 材料

impurity  n. 杂质  inclination  n. 倾斜                 locatev. 定位                                        material marking 下料

inclination test 倾斜试验                               lock washer 锁紧垫片                                   mathematical  a.数学的

inclinev.  倾斜  index  n. 索引                         lofting  n. 放样                                     mathematical lofting skill 数学放样技术

indication  n. 显示  indicator  n. 显示仪                log  n. 计程仪                                        maximum(max.)n. 最大

indicator  n. 指示器                                   logical  a.逻辑的                                     means  n. 手段，工具

indicator light 指示灯                                 long bridge 长桥楼                                    measurement laboratory 计量实验室

indicator valve 示功阀                                 longitudinal  a.纵向的                                measuring meter 测量仪表

inert gas 惰性气体  inertia  n. 惯性                      longitudinal (uniflow)scavenge                     measuring point 测量点

inertia platform 惯性平台                               直流扫气                                               mechanical energy 机械能

inevitable  a.不可避免的                                 longitudinal bulkhead 纵隔舱壁                         mechanical launching 机械下水

initial metacentric height 初稳心高                     longitudinal framing 纵向构架                          mechanical processing 机加工

inject  n. 喷射                                       loop  n. 回路                                        mechanical unit 机械装置

injecting system 喷油系统                               loop antenna 环状天线                                  medium speed  中速

injector  n. 喷油器                                    Loranreceiver 劳兰定位仪                                medium wave 中波

inner bottom longitudinal  内底纵骨                     Loudspeaker  n. 扬声器                                medium-computer  n. 中型（计算）机

inner bottom plate 内底板                              low speed 低速                                       member  n. 构件

inner ring  内环  input  n.v. 输入                      lower deck 下甲板                                     memory  n. 储存器，内存

inspector  n. 质检员                                   LR 英国劳氏船级社                                         memoryand storage system 储存系统

installation  n.  （船上）安装                            lubeoil 润滑油                                        merchant ship  民用船

installation error 安装误差                             lubeoil(L.O.)滑油                                    mercuryn,水银

instancy speed 瞬时速度                                 lubeoil pump 滑油泵                                   meridian  n. 子午线

instrument  n. 仪表,仪器                                lubricant  n. 润滑剂                                  metacentre  n. 稳心

insulating material 绝缘材料                            lubricant film 润滑油膜                                metal recovery 金属回收率

insulation  n. 绝缘                                   lubricating oil 滑油                                 metallic equipment 冶金设备

intake  n. 吸入  intakeport 汲气口                       lubricationsystem 滑油系统                             microclimate  n. 小气候

intakevalve 进气阀  integral casting 整体浇铸              M.E.engineroom 主机舱                                 microcomputer  n. 微机

intention  n. 意向                                    Machinev. 机加工                                      microprocessor  n. 微处理器

intercommunication (intercom)n.                     machinery  n. 机械                                   midship  n.  a.adv. 舯部

内通，内部通讯                                            machinery set 机组                                   military ship 军用船

interfering moment 干扰力矩                             machinery workshop 机电车间                            miller  n. 铣床

intermediatebearing  中间轴承                           machining  n. 机加工                                  minicomputer  n. 小型（计算）机

intermediateshaft 中间轴                               machining workshop 机加工车间                           minimize v. 降至最低

internal combustion engine  内燃机                     magnetic compass 磁罗经                               minus push 负推力

international authorities 国际当局                      magnetic field 磁场                                  minus value 负值

Internet  因特网（国际互连网）                                magnetic needle 磁针                                 miscellaneous  a. 杂项的

introducev.  引进，引入，介绍                               magnetic object 磁性物体                               mobilize v.  动员  model case 样箱

iron powder electrode 铁粉焊条                          magnifier  n. 放大器                                  model plate 样板  model rod 样棒

jig  n. 胎架                                          magnifyv. 放大                                       moderate  a. 中型的

joint design 联合设计                                   magnitude  n. 大小                                   modernenterprisesystem

journal  n. 轴颈                                      mainbearing 主轴承                                    现代企业制度

keel  n. 龙骨   keel plate 龙骨板                        mainengine(ME) 主机                                  modus  n. 操纵法 （pl.modi）

keep station 定位  kerosenetest 煤油实验                  maingenerating set 主发电机组                           monitor v. 监视

keyenterprise 骨干企业                                  MainGroup 1 第一大部分                                  monitoring device 监控装置

kilohertz 千赫  kinetic energy 动能                     mainhull 主船体                                       moor v. 系泊   motivepower  原动力

knot  n. 节   labyrinth  n. 迷宫，曲径                    mainnetwork 主电网                                    motor  n. 电动机

land-based  a. 路基的   landing-place  n. 码头           mainpower station 主电站                              mould loft 放样台  mouth  n. 河口

lapjoint 搭接接头                                       mainswitchboard 主配电板                               moving part 运动件

large-computer(mainframecomputer)  n. 大型 （计  maintenance  n.v. 维护，保养                                   multi-purpose  a.

多用途的，综合的

算）机，主机                                              marker  n. 厂商

multi-stage  n. 多级

layv. 敷设                                            manpower resource  人力资源

mutual benefit 互惠互利

length  n. (一)节，（一）段  level  n. 液位                  management  n. 生产管理

nautical mile 海里

level gauge 液位计   level relay 液位继电器                 maneuver v.  n. 操纵

naval architect 造船设计师

license  n. 许可证  lifeline 生命线                       maneuverability  n. 操纵性

navigating instrument 导航仪器

life-belt  n. 救生圈  life-boat  n. 救生艇                maneuvering console 操纵台

navigating zone 航区

life-jacket  n. 救生衣                                 maneuvering system 操纵系统

navigation computer 导航计算机

中国船员招聘网http://www.crewcn.com

----------------------- 页面 16-----------------------

中国海员之家网站航海英语系列                                               船  舶  轮  机  英  语  集  成                                          第      16   页

navigation equipment 导航设备                         palletizing management 托盘管理                      principle dimensions 主尺度

navigational light 航行灯                            parallel  n. 并联 v. 并车                            process  n. 工艺，流程 v. 加工，处理

navy  n. 海军                                       parallel of generators 发电机并车                     production efficiency  生产效率

navyunderway replenishment ship                   parameter  n. 参数                                 production line 生产线

海军航行补给船                                           part  n. 部件，机械部件                                 production procedure  生产程序

NC cutting machine 数控切割机                          part fabrication 部装                              program  n. 程序

nervecell 神经细胞                                    particle  n. 颗粒                                  projection plane 投影面

nesting  n. 套料                                    party  n.(谈判或合同之)一方                              prolong v.  延长

network  n. 电网                                    passage  n. 通道                                   promotev.  促进，晋升

nil  n. 零，无                                       passageway  n. 通道                                propeller  n. 螺旋桨

NK  日本海事协会                                        passenger-cargo vessel 客货船                       proportion  n. 比例

non–ferrous metal 有色金属                            performance  n. 性能                               propulsion efficiency 推进效力

non-restrictive  a. 自由的，不受限制的                     permanently adv.  永久的                            propulsion plant 推进装置

non-standard product 非标产品                         perpendicular  n. 垂线                             protection type 保护式

non-transparent  a. 不透明的                          personnel  n. 全体人员                               provision  n. 食品

normal displacement 正常排水量                         personnel  n. 人员，人事                              pump  n. 汞

normal shipping 正常营运                              phaseangle 相角                                    purity v. 净化

nozzle  n. 喷嚏                                     phasesequence 相序                                 push rod 顶杆

numbering system 计算系统                             phase–sensitiverectifier                         push-pull magnetic amplifier 推挽磁放大器

numeral  n. 数字                                    相敏整流器                                            pyramid method 正装法

numerical control (NC)数控                          physical quantity 物理量                             quality assurance 质量保证

numerical control cutter 数控切割机                    physical-chemical experiment                      quality control 质量控制

nut  n. 螺母                                        理化实验                                              quality management 质量管理

observation  n. 观察                                physical-chemical experimental center             quality policy 质量方针

occasion  n. 盛事，盛举                                理化中心实验室                                           quay  n.(顺岸式)码头

ocean-going vessel 远洋船                            pillar  n. 支柱                                     quiescent  a.安静的

oceanographic research vessel 海洋调查船               pilot  n. 驾驶员，领航员，舵轮                             radar  n. 雷达

offshore service 近海作业                             pipeconnection 管子接头                              radio beaconstation 导航台

oil charging piping 注油管系                          pipeflange 管子法兰                                  radio communication  equipment

oil consumption 油耗                                piping system 管系                                  无线电通讯设备

oil filling port 注油口                              piston pin 活塞环                                   radio directional finder 无线电测向仪

oil mist 油雾                                       piston pin 活塞梢                                   radio message 无线电报

oil refinery 炼油厂                                  piston stroke 活塞冲程                               radio receive 无线电接收机

oil tanker 油船                                     pitch  n. 纵摇                                     radio room 报房

oil-resistant  a.耐油的                              plan  n. 图纸                                      radio station  电台

oil-tight  n. 油密                                  plane  n. 平面                                     radio transmitter 无线电发信机

Omega/satellite integrated navigation instrument  奥  planev. 整平                                    radio wave 无线电波

米加/卫星导航系统                                         planing machine 校平机                              range  n. 航程

one-sidewelding 单面焊接，双面成形                         plant  n.  （成套机电）设备                              rangev. 测距

one-way  a.单向的                                    platform  n. 平台                                  rangedisplay 航程显示器

open chamber 开放式燃烧室                               pneumatic tool 气动工具                              rangeunit 航程装置

open circulation 开放循环                             pointing of direction 指向                         rated power 额定功率

opening  n. 开口                                    poisonous gas 有毒气体                               rated value 额定值

operating cycle 工作周期                              pollution  n. 污染                                 reaction  n. 反作用力

operation  n. 施工                                  poop  n. 艉楼                                      reading  n. 读数

operation  n. 运行，运转                               port  n. 左舷                                      receiver  n. 接收器

operation surroundings 作业环境                       portablelight 手提灯                                reciprocating movement 往复运动

operator  n. 操纵员                                  postdoctoral centre 博士后工作站                       rectification  n. 矫正，整顿

opportunity  n. 机遇                                potablewater 饮用水                                 rectifyv. 整流，滤波

optical projector 光学仪器                            pourv. 涌入，源源不断                                   reduction gear 减速齿轮

optics  n. 光学                                     power  amplifier 功率放大器                           reduction gearbox 减速齿轮箱

orbit  n. 轨道                                      power plant 动力装置,(火力)电厂                          reduction unit 减速装置

order  n.v.  订单，定购                                power station  电站                                reduction withanasternclutch

oscillation  n. 振荡                                power supply  电源，供电                               带到车离合器的减速

oscillation current 振荡电流                          power system  电力系统,动力系统                          reefer  n.  （俗）冷藏船，冰箱

outboard adv. 向舷外                                 practice  n. 习惯做法                                reflect v. 反射

outerappearance 外观                                preamplifier  n. 前置放大器                           refrigerating plant 制冷装置

outerring 外环                                      pre-combustion chamber                           register  n.(机)验船师

outfitting  n. 舾装                                 预燃燃烧室                                            register  vt. 登记，注册

output  n. 输出                                     pre-heat v. 预热                                   regulation  n. 登记

overload v. 过载                                    pressure container 压力容器                          regulator  n. 调整器

owner  n. 船东                                      pressure relay 压力继电器                             relativehumidity 相对湿度

owner’srepresentative                             pressure sensor 压力传感器                            relativemotion 相对运动

船东代表                                              pressure tank 压力柜                                relay contactor 继电器

oxide  n. 氧化皮                                     pretreat v.  预处理                                 remains  n. 残余

paint  n. 油漆                                      primary radio transmitter                        remotecontrol 遥控

pain-taking  a.艰巨的                                主无线电发信机                                          remotecontrol station 遥控站

painting  n. 涂装                                   primemover 原动机                                   rescuev.  n. 救援

painting  n. 涂装，油漆工艺                              primer  n. 底漆                                    rescuefrequency 救援频率

primer painting 涂底漆

中国船员招聘网http://www.crewcn.com

----------------------- 页面 17-----------------------

中国海员之家网站航海英语系列                                              船  舶  轮  机  英  语  集  成                                        第      17   页

rescuetransmitter 救援发信机                          servicetank  日用柜                                stability  n. 稳性

resemblev. 相似                                    servo motor 伺服电动机                               stabilizer  n. 减摇鳍

reservebuoyancy 储备浮力                             settlev. 沉淀                                     stabilizing unit 减摇装置

reservoir  n. 容器   resistance  n. 阻力             settling tank 沉淀柜                               staffmember 职员

resistanceheat  电热阻  rest v.  靠左                 shaft bracket 艉轴架，人字架                           stage  n. 级

retaining washer 保护垫片                            shaft system 轴系                                 stainless steel 不锈钢

retakev. 回收，取回                                   shapeprocessing 成形加工                            stand v. 经受

reversal  n. 换向                                  shearmachine 剪切机                                standard  n. 标准

reverse v.  反向逆转                                 shed v. 放射，散发  sheer  n. 脊弧                     standard displacement 标准排水量

reverse power 逆功率                                sheet plate 薄板  shell  n. 壳板                    stand-by  n. 备用

reversing system 换向机构                            shell plating 外壳列板                              stand-by generating set 备用发电机

revolution  n. 旋转                                shell structure 外板结构                            starboard  n. 右舷

rigid  a. 刚性的   ring seam 环缝                     ship equipment 船舶结构                             start v. 动身，出发

rock arm 摇臂  roll  n. 横摇                         ship general 总体  ship outfitting 船舾             starting system 起动系统

roller machine 滚床                                ship system 船舶系统                                starting valve 启动阀

room  n. 余地  rope  n. 缆索                         shipbuilding  n. 造船                             statev.  说明

rotary movement 旋转运动                             shipbuilding industry 造船工业                      state-specified  a.部颁的

rotatev. 旋转                                      shipbuilding technology research institute 造船工艺  station v. 驻扎

rotating direction 旋转方向                          研究所                                             steadiness  n. 稳定性

rotation  n. 旋转度  rotor  n. 转子                   shipping  n. 航运                                 steam&aux.boiler system

rough sea 波涛汹涌  roughness  n. 粗糙度                shipyard(yard)n. 船厂                             蒸汽与副锅炉系统

routine  n. 例行公事                                 shop trial 车间实验                                 steel platepretreatment 钢板预处理

rpm 转速   rudder  n. 舵                            shore electricitybox 岸电箱                        steel structure 钢结构

rudder angleindicator 舵角指示器                      short circuit 短路  short wave  短波                steel wire 钢丝

rudder carrier 舵承，舵托                             short-range  a.短途的                              steering gear 操舵装置

rudder stock 舵轴，舵杆                               shot-blast v. 喷丸                                steering gear 舵机

rudder stopper 舵角限制器                             shot-blasting 喷丸处理                              steering gearroom 舵机房

rules  n. 规范，规则                                  side  n. 船侧  side girder                        steering mechanism 操舵机构

running  n. 经营管理                                 sidelight 舷灯                                    steering wheel 舵轮

rust preventative 防锈剂                            sideplate 弦侧板                                   stem  n. 艏柱

rust prevention 防锈                               sidestructure 船侧结构                              stern  n. 船艉，艉柱

rust removal 除锈  rust-proof  a.防锈的               signal  n. 信号  signal light 信号灯                 sterntube 艉轴管

safeguard v.  捍卫                                 signal processor 信号处理器                          stiffener  n. 扶强，加强筋

safetyvalve 安全阀  salt content 含盐量                silicon  n. 硅                                   storage tank 贮存柜

sanitary water 卫生水                               silicon control rectifier(SCR)可控硅               store-room  n. 储藏室

saturated steam 饱和蒸汽                             singlebottom 单底                                 straight line 直线

scavenge v.  n. 扫气  scavengebox 扫气箱              single-action  a.单作用                            straight seam 直焊缝

scavenge flow 扫气气流                               single-rudder  n. 单舵                            strength test 强度试验

scavenge pattern 扫气型式                            single-stage  n. 单级                             stringer  n. 纵通材

screen  n. 荧光屏                                   single-screw  n. 单桨                             structural material  结构材料

screw shaft 螺旋桨轴                                 sitearchitect 现场造船师                             structure  n. 结构，构件

sea damage 海损                                    sitesupervisor 现场监控师                            stud  n. 螺柱

sea trial 试航                                     sketch  n. 草图                                   stuffing box 填料函

sea water (SW)海水                                 slide-block  n. 滑板，导块                           subwayshield 地铁盾构

sea-chart room 海图室                               sliding distance 滑行距离                           suck v. 吸入

seakeeping performances                          slipway  n.(倾斜)船台                               suction(induction) stroke 汲气冲程

航海性能，试航性                                         slipwaytaper 船台斜面                               suctionport 吸入口

seal  n.v.  密封                                   small metacentric angle 小倾角                     sufficient  a.足够的，充足的

sealing agent 密封剂                                socialist market economy                        sum  n.(数)二树之和

sealing gasket 密封垫片                              社会主义市场经济                                        supercomputer  n. 巨型（计算）机

sealing ring 密封圈                                 software  n. 软件  soil  n. 土壤                    superstructure  n. 上层建筑

search light 探照灯                                 SOLAS  国际海上人命安全公约                               supervision  n. 监督,监造

seasick  a.晕船                                    SOS 遇难信号                                        supply vessel 补给，工作船

seat  n. 座                                       sound energy 声能                                 support  n. 支撑物

seating  n. 基座                                   sound insulation 隔音                             surfacetreatment 表面处理

section  n. 总段                                   sound power telephone 声力电话                      surveyor  n.(船)验船师

self excitation  自励                              sound speed 声速   sound wave 声波                  survive v.  幸存，死里逃生

self-designed  a.自行设计的                           sounder  n. 测深仪                                 sustainv. 支撑，支持

self-regulated device  自我调节机构                    sources of power supply 能源                      swirl chamber 涡流式燃烧室

semi-conductor  n. 半导体                           space  n. 舱室                                    swirl resistance 涡流式阻力

SEMT of France 法国热机协会                            space  n. 空间                                    switch  n. 开关

senior engineer 高级工程师                            sparegears 备品                                   symbol  n. 符号

sensibility  n. 灵敏度                              spareparts(spares)备件                            symmetrical  a.对称的

separation  n. 分离                                special power supply 特种电源                       synchro (selsyn)n.  自整角机

separator  n. 分离器                                speed indicator 航速指示器                           synchro signal transmitter  自整角机讯号发送器

serialize  vt.使……成系列                             speed reduction 减速                              synchronous device  同步装置

service  n. 公共基础设施                               speed servo system 速度随动系统                       synchronous follower  同步随动件

serviceengineer 服务工程师                            spring  n. 弹簧                                   talent  n. 人才，有才能的

servicelife 使用寿命                                 squeeze  n.v. 挤压                                technical staff 全体技术人员

中国船员招聘网http://www.crewcn.com

----------------------- 页面 18-----------------------

中国海员之家网站航海英语系列                                                 船  舶  轮  机  英  语  集  成                                           第       18   页

technical force 技术力量                                thesystem software 系统软件                            velocity  n. 速度

technical service 技术服务                              thetotal longitudinal bend 总纵弯曲                    ventilating pipe 通风管

technical specification(spec)技术规格书                  thetotal longitudinal strength 总纵强度                ventilation &air-conditioning system

technical term 技术术语                                 thetotal tonnage 总吨位                               通风与空调系统

telegraph  n. 传令钟                                   thermal mechanism 热力机械                             ventilator  n. 通风机

teleprinter  n. 电传打字机                               thermal stress 热应力                                 vertical  a. 垂直的，直立式的

teleperaturerelay 温度继电器                             thermometer  n. 温度计                                vertical seam 垂直焊缝

temporarily adv. 临时地                                thread v. 攻螺纹                                      vertical welding 立焊

temporaryemergency power supply                     thrust bearing 推力轴承                                vibration  n. 振动

临时应急电源                                              thrust end 推力端                                     viscosity  n. 粘度

terminal  n. 终端                                     thrust ring 推力环                                    visiblerange 视距

testing  n. 调试                                      thrust shaft 推力轴                                   visual telegraph 灯光传令钟

testing facilities 测试设备                             thyristor  n. 硅可控整流器，可控硅                           visual-acoustical signal 灯光音响信号

testing instrument 测试仪器                             tier  n.  （船）层                                     voltage  n. 电压

test &trials 试验与试航                                  TIG 钨极惰性气体焊                                        voltagelatching  电压锁定

TEUreefercontainer ship 冷风集装箱船                      tightness test 密性试验                                voyage  n. 航行

theambient air 大气                                   time  vt. 确定……的时间                                  wasteheat 余热  water head 压头

theapplicationsoftware 应用软件                         timing gear 准时机构                                   water inlet pipe 进水管

theblock coefficient 方型系数                           title  n. 职称，头衔                                    water jacket 水套

thebrakehorsepower (BHP)                            tonnage  n. 吨位                                     water pressure test 水压试验

轴马力，制动马力                                            top people 上层人物                                    water supply 水源，自来水

thebreath moulded 型宽                                top sideplate 弦侧顶板                                 water supply system 供水系统

thecentral processing unit (CPU)                    torsional vibration 扭振                             water vapour 水蒸气

中央处理单元                                              torsional moment 扭距                                waterline 水线

the centralized control room (the control room)集控  TQC全面质量管理                                           watertight  a. 水密的

室                                                   transceiver  n. 收发报机                               water-tight test 水密试验

thecontrollablepitch propeller (CPP)                transferpump 输送泵                                   waveimpact 波浪冲击力

可调螺距桨                                               transistor amplifier 晶体管放大器                        wave-forming (wave-making) resistance 兴波阻力

thecritical path method (CPM) 各                     transistor controller  晶体控制器                       wear  n.v.  磨损

种计划节点配合                                             transistor loop  晶体管回路                             weather post 露天部位

thedata base management system (DBMS)数据库管  transmitter  n. 发射机,发送器                                     weight calculation 重量计算

理系统                                                 transportation  n. 输送                              welder  n. 焊工，焊机

thedepth moulded 型深                                 transversal  a. 横向的                                welding  n. 焊接

thedesignwater plane 设计水线面                          transversal bulkhead 横隔舱壁                          welding laboratory(lab)焊接试验室

thedesignwater planecoefficient                     transversal scavenge 横流扫气                          welding machine 焊机

设计水面线系数

transversal stability 横稳性                          welding procedure 焊接方法 （工艺）

thedisplacement coefficient 排水量系数

treatment plant 处理装置                               welding seam 焊缝

theearthmagnetic field 地球磁场

trend  n. 趋势                                       welding wire 焊丝

theeffective horsepower 有效马力

trial-and-error  a.                                well adv.  完全有理由

thefiremain 消防总管

反复的通过试验找出错误的                                       wheel steering  随从操舵，舵轮操舵

thefixed pitch propeller  固定螺距桨

trim  n. 纵倾                                        wheel house  n. 驾驶室

thefuturetype 未来型

trunk-piston  n. 筒形活塞                              whereby adv. 靠那个

thegraphic processing software

T-typejoint T 型接头                                  wing buoyant tank 减摇水舱

图像处理软件

tuition  n. 学费                                     wirecable 钢索

theintertia navigation system

惯性导航系统                                              turbineoil 透平油                                     work  n. 功

theintegral stud anchor chain 整体锚链                  turbocharger  n. 涡轮废气增压器                           working condition 工况

thelanguagesystem 语言系统                              turning ability 回转性                                working principle 工作原理

thelength B.P.两柱间长                                  turning circle 回转半径                                working schedule 生产进度

thelength overall 全长                                turning gear 盘车机构                                  working site 现场

thelengthW.L.水线长                                    turning motion 回转                                  workmanship  n. 工艺，流程

theliving quarters 生活区                              twenty-foot equivalent unit (TEU)                  X-rayphoto  X 光照片

thelongitudinal prismatic coefficient 纵向菱形系数  20英尺国际标准集装箱                                              yaw  n. 偏航角

themetacentreof transversal inclination 横倾稳心        twin-engine incoporation 双机并车

twinkle  v. 闪烁

themiddlelongitudinal cross section

舯横剖面                                                twin-rudder  n. 双舵

the midship transversal cross section coefficient  舯  twin-screw  n. 双桨

横截面系数                                               two-way  a. 双向的

thenet registered tonnage 净登记吨位                     ultrashort wave 超短波

theNorthPole 北极                                     UMS 无人机舱

theofficeautomation (OA)办公自动化                       under voltage 欠电压

theoperating system (OS)操作系统                        uneven  a. 不均匀

thepainting outfitting 涂装                           uniform  a. 均匀的

theparties concerned 有关方面                           unload v. 卸载

thepropulsion plant 推进装置                            upper deck 上甲板                                     船体制图常用名词术语英汉对照

therated frequency 额定功率                             upset v.(船只)倾覆                                     A-bracket   人字架

therated horsepower 额定马力                            vacuum  n. 真空                                      after peak  尾尖舱

theroll period 横摇周期                                 validate  vt.  (使)生效                               after peak bulkhead        尾尖舱壁

thesatellitenavigation system                       valvemechanism  阀机构                                After perpendicular        尾垂线

卫星导航系统                                              vaporize v. 汽化                                     air hole     透气孔

中国船员招聘网http://www.crewcn.com

----------------------- 页面 19-----------------------

中国海员之家网站航海英语系列                                    船  舶  轮  机  英  语  集  成                               第     19   页

anchor 锚                                 deck house  甲板室                          keelson 内龙骨

angle bar   角钢                           deck line at center   甲板中线                intercostal center keelson 间断中内龙骨

assembled molded lines 理论线               deck line at side     甲板边线               keel line   龙骨线

auxiliary tank     调节水舱                  deck longitudinal     甲板纵骨               keel strakeK 行板,平板龙骨

ballast 压载                               deck stringer         甲板边板               knuckle lines         折角线

ballast water tank  压载水舱                 depth moulded        型深                  L iron     不等边角铁、不等边角钢

base line   基线                           derreck platform     起货机平台                length between perpendiculars   两柱间长

base plane  基平面                          design draft         设计吃水                 length overall       总长

beam       横梁                            designed water line  设计水线                 life boat   救生艇

beam knee   梁肘板                          Diagonal   斜剖线                            life jacket救生衣

berth 码头                                 domed bulkhead       球面舱壁                 life raft   救生筏

bunk 舱位                                  double bottom        双层底                  life-saving suit     救生服

bilge  （船底）污水                            doubling plate       复板                   lightening hole      减轻孔

bilge bracket     舭肘板                    draft molded         型吃水                  lines plan  型线图

bilge keel  舭龙骨                          draught marks 吃水线 （美作：plimsoll mark）  longitudinal bulkhead  纵舱壁

bilge strake      舭列板                    draftsman   制图员                           transverse bulkhead  横舱壁

blade 桨片                                 drain hole  流水孔                          wash bulkhead         制荡舱壁

oars 桨，橹                                 drain well  污水井                          watertight bulkhead   水密舱壁

block division plan  分段划分图               drawings for metal hull of ships          longitudinal         纵骨

bow, prow 船首                             金属船体制图                                    longitudinal section plan 纵剖面图

body lines  横剖线                          duck keel   箱形中底桁                         longitudinal section   纵剖面

bottom center girder  中底桁                end snip for stiffeners 型材端部削斜            longitudinal section in center plane

bottom flat line     平底线                 engine casing        机舱棚                  中纵剖面图

bottom frame         船底肋骨                engine room          机舱                  upper deck 上甲板 lower deck   下甲板

bottom plate         船底板                 expansion trunk      膨胀阱                  orlop 最下层甲板 quarter deck 后甲板

bottom side girder   旁底桁                 face plate  面板                            second deck第二甲板

bracket    肘板                            fairing of lines     型线光顺                platform deck        平台甲板

bracket floor        框架肋板                fender     护舷材                            strength deck        强力甲板

breadth molded       型宽                  Fine dash line       细虚线                  superstructure       上层建筑

bridge deck 驾驶甲板                         finished plan        完工图                  sponson deck         舷伸甲板

bulb plate  球扁钢                          flat bar   扁钢                            weather deck          露天甲板

bulwark    舷墙                            flat bulb steel      球扁钢                  office deck 高级船员甲板

bulwark top line     舷墙顶线                flat section         平面分段                main deck center line  主甲板中线

buoy ring   救生圈 butt weld   对接焊缝         floor      肋板 fore peak 首尖舱              main deck side line   主甲板边线

buttock    纵剖线                           forecastle  首楼                           poop    尾楼 poop deck 尾楼甲板

buttock line         纵剖线                 forecastle deck center line  首楼甲板中线      poop deck center line  尾楼甲板中线

cabin plan  舱室布置图                        forecastle deck side line 首楼甲板边线         poop deck side line  尾楼甲板边线

cabin, stateroom 客舱                      forward perpendicular  首垂线               main flame  主肋骨 manhole人孔

camber     梁拱                            rib 肋骨 frame       肋骨                    margin plate          内底边板

camber curve(line)   梁拱线                 frame spacing  肋骨间距                      mess deck   餐厅甲板

cant beam   斜横梁 cant frame   斜肋骨         midship frame 中部肋骨                       middle-line plane     中线面

capacity plan        舱容图                 tweendeck frame       甲板间肋骨              midship section       中横剖面

captain deck         船长甲板                frame body plan      肋骨型线图               midship section plan  中横剖面图

cargo hatch 货舱口 cargo hold   货舱          frame line  肋骨线                          midstation  中站

center keelson       中内龙骨                frame number         肋骨号数                midstation plane      中站面

centerline bulkhead  中纵舱壁                freeboard  干舷                            model frame line plan  肋骨型线图

central longitudinal section    中纵剖面   French curve            曲线板                molded hull surface   船体型表面

certer line船体中心                          front elevation      正视图                 molded line型线

chain locker         锚链舱                 full thick line      粗实线                 molded surface        型表面、理论表面

clearance hole       通焊孔                 general arrangement plan 总布置图            node detail plan      节点详图

cofferdam   隔离舱                          general structure plan 基本结构图              offset table         型值表

collision bulkhead   防撞舱壁                girder of foundation   基座纵桁               offsets   型值

combination cast and rolled stem  混合首柱   gunwale angle        舷边角钢                 outboard profite    侧面图

compass 罗盘                               gusset plate         菱形板                 panting beam          强胸横梁

bridge deck                              H bar   工字钢 half beam 半梁                 pillar     支柱

compass deck         罗经甲板                half breadth plan    半宽水线图               plan view   平面图

connecting line for floor end on top 肋板  hatch coaming        舱口围板                plane bulkhead       平面舱壁

边线                                       hatch end beam       舱口端横梁               plate keel  平板龙骨

construction plan    结构图，施工图             hatch side cantilever  舱口悬壁梁             platform   平台

corner weld角焊缝                           hatch side girder    舱口纵桁                profile    外廓线

corridor   通道、走廊                         horizontal girder    水平桁                 railway line          轨道线

corrugated bulkhead  槽形舱壁                horizontal stiffener  水平扶强材              reverse frame         内底横骨

corrugated transverse bulkhead plan      ice light water line   冰区轻载水线            rounded lines         转圆线

槽形横舱壁图                                   ice load water line  冰区满载水线              rudder 舵

crosstie   撑杆                            imaginary line       虚线、假想线              rudder post舵柱

Dat-and-dask fine line 细点划线              inner bottom plate   内底板                  tiller 舵杆

deadrise   底部升高、船底倾斜度                    inner surface        内表面                  scantling draft      结构吃水

deadrise angle       船底横升角               intermediate frame   中间肋骨                 screen bulkhead      轻舱壁

deck girder 甲板纵桁                         keel 龙骨                                   seam      边接缝

中国船员招聘网http://www.crewcn.com

----------------------- 页面 20-----------------------

中国海员之家网站航海英语系列                                          船  舶  轮  机  英  语  集  成                                    第      20   页

shaft tube  尾轴管                               12． 我们正在安装热水供 暖系统 。 We are                        work well.

port 左舷                                           installing   the   hot   water   heating  45． 阀体内部应涂上漆。 The inner part of the

starboard 右舷                                      system.                                       valve body  should be coated with  the

sheer       舷弧                                13． 生活用水系统 出了什么毛病 ？ What’s                        paint.

sheer at after perpendicular   尾舷弧                wrong with the domestic water system?    46． 尾门需要重新安装。 The stern door should

sheer at forward perpendicular  首舷弧           14． 柱塞应从套筒里抽 出来 。 The plunger                     be reassembled.

sheer line  舷弧线                                   should be withdrawn from sleeve.         47． 起货机已经安装好了。 The cargo winch has

sheer strake           舷顶列板                   15． 磨削缸套， 除去刮痕。 Remove the scuffings              been installed.

shell bossing          轴包套                        by grinding the linear.                  48． 盘 车 机 坏 了 。 The  turning  gear  is

shell expansion plan   外板展开图                  16． 做一个拆装汽缸盖螺帽用的环形扳.Make a rindga maged.

shell plate外板                                     spanner for the nuts of the cylinder cove4r9.．   我们正在安装起锚设备。 We are installing

side keelson           旁内龙骨                   17． 环形扳手在 哪里 ？ Where  is  the  ring               anchor handling machinery.

side plate  舷侧外板                                  spanner?                                 50． 检查一下造水机。Make a check of the

side stringer           甲板边板                  18． 环形扳手在我这里。The ring spanner is                  fresh water generator.

single bottom          单底                         in my hand.                              51． 锚链轮应与锚链贴合。The wildcat should

size of collar plate   补板尺寸                   19． 你需要扳手吗？Do you need the spanner?               be fitted in with the anchor chain.

size of notches        切口尺寸                   20． 请把环形扳手给我。Please give me the   52． 锚机刹车失灵。 The break of the windlass

snip end    端部削斜                                  ring spanner.                                 is out of order.

solid floor 主肋板                               21． 请检查一下油水分离器。Please inspect  53． 请 将 锚 机 修 一 下 。 Please  make  the

station ordinates      站线                         the oil/water separator.                      windlass repaired.

stations    站                                     1号起重机已经拆除。 No.1 cargo winch has               变幅马达用来升降吊臂。 The luffing motor

22．                                          54．

stiffener   加强筋；扶强材                               been removed.                                 is  used  for  raising  or  lowering  the

T-bar       T 型材                              23． 起重机已经安装。Cargo winch has been                  job.

thick dash line        粗虚线                        installed.                               55． 起重机安装好 了没有 ？ Had  the  cargo

thick dash-and-dot twin point line            24． 请仔 细检 查一 下 。 Please  inspect  it              crane been installed?

粗双点划线                                 carefully.                               56． 请将 这个 穿舱件 改成水密 的 。 Please  change

thick dask-and-dot line粗点划线                       鼓风机应装在哪儿？Where is the blower                  penetrating piece into watertight

25．

topside tank           顶边舱                        installed.                                    construction.

torsion box            抗扭箱                    26． 所有阀闸都应拆除。 All the gates have to  57． 先 进 行 管 道 分 段 预 装 。 Go  on  pre-

transom plate          尾封板                        be disconnected.                              installation of piping in hull section

transom stern          方型尾                    27． 泵打不出压力。The pump fails to build                first.

tripping bracket       防倾肘板                       up pressure.                             58． 板块连接 有 问题 。 There’s  something

vertical girder        竖桁                         拆开泵检查密封。Dismantle the pump to                 wrong with the plate connection.

28．

vertical stiffener     垂直扶强材                      check its seal.                          59． 这个 箱柜 怎么 没有 安装 泄放 阀？ Why

water lines水线 water plane水线面                  29． 在通海箱上安上 2 块锌板。Fit up two                      didn’t you fit a drain valve on this

watertight floor       水密肋板                       pieces of zinc slabs in the sea chest.        tank?

web         腹板 web beam 强横梁                   30． 我们已经完成管路系统的安装。We have  60． 这样布置给以后操作及维护工作带来不便。

web frame   强肋骨；特大肋骨                              complete   the   installation   of   the      Such an arrangement is inconvenient to

weld size   焊缝尺寸                                  piping.                                       the future operation and maintenance.

welding symbols        焊缝符号                   31． 管路出了什么问题？What’s wrong with  61． 控制箱振动太 厉害 。 The  control box

wooden structure       木结构                        the piping system?                            vibrates seriously.

zig-zag welding        交错焊接                       管子漏气。 There is the air leakage from           我们在安装避雷装置。We are installing

32．                                          62．

the pipe.                                     the lightning arresters.

船 用 机 械 设 备 安 装 用 语  （ English  for  33． 恒温器动作迟钝 。 The motion  of  the  63． 避雷装置安装在哪里 ？ Where are  the

Installation of Marine Machine）                   thermostat is stagnant.                       lightning arresters installed?

1． 锚机可以使用了。The windless is ready  34． 制冷设备失灵了。 The refrigerating plant  64． 装上散件并定位好。Loading piece parts

for use.                                     is out of operation.                          and positioning well.

2． 所以螺母应该用冲击锤上紧。All the nuts  35． 使锌板与外壳接触 良好 Bring the zinc  65． 阀门传动装置安装在另一舱室。The valve actuating

should be tightened up with an impact        plates  into  good  contact  with  the        device is installed in another room.

wrench.                                      casing.                                  66． 蒸汽室的空间太大。 The size of the steam

应把螺旋桨拆下。 The propeller should be             安全阀是成对安装的。Relieve valves are                  chest is too big.

3．                                            36．

dismantled.                                  mounted in pairs.                        67． 这些结构的焊接变形太严重了。 The welding

4． 机舱通风应改装。The ventilator in the  37． 安全阀安装在锅炉上。Relieve valves are                              distortion  of  these  structure  is  too

engine room should be refitted.              mounted on the boiler.                        serious.

5．  液压缸应镗圆。The hydraulic cylinder  38． 这台舵机是什么型号的？What type is the  68． 螺旋桨的安装已经完成。The mounting of

should be bored round.                       steering gear?                                propeller has been finished.

操舵装置仍偏差 2 度。The steering gear                这种舵机是电动液压式的。This steering                     请进行螺旋桨胶合连接。Please bond the

6．                                            39．                                          69．

still has a deviation of 2 degrees.          gear is of the electrohydraulic type.         propeller to shaft.

7． 请检查一下尾轴锥形部分。Please check  40． 舵机是船上很重要的设备之一。                                            70． 螺旋 桨 液 压 无 键 连 接 。 Mounting  of

the conical part of the tailshaft.           The steering gear is one of the most          propeller by hydraulic jack.

8．  舵机和舵轮的运动不一致。The steering                      important devices in the ship.           71． 螺 旋 桨 的 螺 距 需 要 矫 正 。 Check  of

gear is not in step with the steering  41． 舵机的主要功能是控制船舶的航向。The main funcptrioonp eller pitch is needed.

wheel.                                       of the  steering  gear  is to  control  the  shi螺旋桨锥p’s  孔修正。Scrapping of propeller

72．

9． 舵角指示器的误差太大。The error of the                    course.                                       boss.

rudder angle indicator is too large.     42． 这台制冷机的能量是多少？What is the  73． 计算法轴系校中。Centering of shafting

10． 指示 器 应 调 整 。 The  indicator water             capacity of this refrigerator.                by calculation method.

system had been installed.               43． 螺旋桨出了什么问题？What’s wrong with  74． 轴承 负荷 法轴 系 校 中 。 Centering  of

11． 给水系统已经安装完毕。The feel water                     the propeller?                                shafting by loading method.

system had been installed.                   螺旋桨工作不稳定。The propeller can’t                  平轴法轴系校中。Centering of shafting

44．                                          75．

中国船员招聘网http://www.crewcn.com

----------------------- 页面 21-----------------------

中国海员之家网站航海英语系列                                           船  舶  轮  机  英  语  集  成                                     第      21   页

by direct connection.

76． 尾轴管轴承塑料喷漆。 Spraying of plastic

on stern tube bearing.

77． 轴系中心定位块在那里。The center block

for shafting alignment is over there.

下汽缸和轴承座找正。 Alignment of bottom

78．

casing and bearing seating.

79． 这里需要进行螺栓热紧。Tightening of

bolts in hot state is needed here.

80． 螺旋形卷管机在哪里？Where is the pipe

coiling machine?

我们更换了两盏探照灯。We have replaced

81．

two searchlights.

82． 请脱 开盘 车机 。 Please  take  out  the

engine turning gear.

83． 将盘车机合上。 Put in the engine turning

gear.

84． 启动循环泵。Start up the circulating

pump.

85． 脱 开 操 纵 联 动 机 构 。 Disengage  the

maneuvering linkage.

86． 开阀/关阀。Open/close the valve.

87． 有没有什么机械需要送到车间去？Is there

any machinery to be moved to the workshop?

88． 你们何时开始安装起货机？When will you

begin to install the cargo winches?

螺旋桨太大移不动。The propeller is too

89．

big to move.

90． 在两端盖板装好后应对内部管子进行水动力实

验。 After the end covers are fitted back,

a  hydraulic  test  should  be  applied  to

the inside tubes.

91． 设备 修 理好 了，你可 以使用 了 。 The

machinery has  been  repaired. You  can

use it now.

92． 你们有这部压缩机的整套配件吗？Do you have a complete

set of spare parts for this compressor?

93． 滑油泵的位置不适当。 The position of the

lube oil pump is not suitable.

中国船员招聘网http://www.crewcn.com